## Slide 1: Nuclear Energy Part 2
Boeker & Grondelle Chap. 5
4 September 2013

## Slide 2: Reference Group
Volunteers???? Three preferred.
2 meetings during the year (about 1/3 and 2/3 through course)
Serve as contact point between students and lecturer
  For example, if there arises a problem, or students want to see something different in the course, the reference group can bring this to my attention.
At the break, leave your name and email with me

## Slide 3: Last Time
The basis for nuclear power
  Binding Energy, fission/fusion energy release
Basic principles of fission
  Nuclear equations, cross section for fission, thermal vs. fast neutrons
Chain reactions
  Use to sustain fission reactions, number of neutrons per fission, how to control number of free neutrons
Control
  Fast growth times with prompt neutrons, Saved by the fraction of secondary neutrons (9 sec later)
T steam ~300oC
So   34% (Carnot)

## Slide 4: Basis
235U
X
Y
=2.43
Fast neutrons
+
215 MeV
k 1.1
Moderator
H2O, D2O, Graphite…
k= 1
Reactor wall
238U
other surfaces
Control Rod
tuning
Thermal neutron
Thermal neutron
Thermal neutron
Heat to heat engine
L=10-4 s
c=0.1 s
L*=9 s
*c = 50 s
Ln(Nneutrons)
time

## Slide 5: Today
Fission power plants
  Real reactors
    BWR, PWR, CANDU, HTGR
    Burners, converters and breeders
The Uranium cycle
Safety
Accidents

## Slide 6: The various nuclear systems
Not all nuclear power plants are the same.
There are various systems which are characterised by three basic
elements:
fuel: enriched or natural uranium; plutonium, thorium (rarely used).
moderator: ordinary water; heavy water; graphite.
heat exchanger fluid: ordinary water either pressurised or boiling; heavy water; carbon dioxide; sodium; helium.
The pressurized water reactor (PWR) is the most widely used reactor
system in the world.

## Slide 7: Pressurised water reactor
Higher pressure: higher boiling point: warmer water (320C @150 bar)
Efficiency : 34%

## Slide 8: Boiling water reactor
Efficiency: 33%

## Slide 9
From the Institution of Engineering and Technology

## Slide 10: Burners, converters and breeders
Reactors such as BWR and PWR are called converters: They produce 233Th and 239Pu which could be used to run reactors from the reaction of FAST neutrons.
That is, 233Th and 239Pu are fissile with fast neutrons
Conversion Ratio = (fissile material produced) / (fuel burned) is used to classify reactors.
If the conversion ratio is 0 the reactor is a burner, if it is between 0 and 1 it is a converter and if it is larger than 1 it is a breeder.

## Slide 11: Breeders
The breeder produces more fuel than it burns.
In a breeder extra 238U is put into the reactor core, to make 239Pu.
In a fast breeder reactor (FBR), the chain reaction is sustained by fast neutrons (no need for moderator).

## Slide 12: Breeder advantages and disadvantages
+ Breeder power plants might not run out of fuel in 50 000 years
+ With sea water extraction of Uranium, breeder power plants would last as long a the Earth Sun relationship
Pu is used as a fuel, but Pu is also used in nuclear weapons
The radioactive fuel needs to be reprocessed, to extract the bred materials
  Safety issues during transportation and handling (environment, health, nuclear weapons)
There have also been practical problems

## Slide 13: Today
Fission power plants
  Real reactors
    BWR, PWR, CANDU, HTGR
    Burners, converters and breeders
The Uranium cycle
  Nuclear fuel and replenishment
Safety
Accidents

## Slide 14: Uranium cycle
Uranium
  A hard, grey metal
  Relatively widespread in the earth's crust
  Found as different mineralogical forms in both granite and sedimentary rocks.
In the mines uranium is mostly found as oxides.
The richer ores have 1-4 kg uranium per 1000 kg of ore.
This is processed locally producing “yellow cake” with ~80% U3O8.

## Slide 15: Uranium fuel
The "yellow cake"
  not clean from a nuclear point of view
  Wrong chemical form for use as a reactor fuel directly.
Further treatment in two stages:
  Chemical purification to very pure uranium oxide
  Mixed with hydrofluoric acid to produce uranium tetrafluoride (UF4).
  UF4
    Used to make the uranium metal used in un-enriched uranium reactor systems
    Used to make uranium hexafluoride (UF6) which is intended for enrichment.

## Slide 16: Example
UF4 or enriched UF6 precipitated into uranium oxide powder
Compressed into pellet
Stack and seal into a rod
Collect rods into a fuel assembly
Example: 900 MWe pressurised water reactor core has: 157 fuel assemblies, each with 264 rods, total of ~11 million pellets
Each pellet  2.5 tonnes coal

## Slide 17: Enrichment
1. Gaseous diffusion
Pass gaseous uranium hexafluoride (UF6) through fine membranes with billions of pores.
The 235U isotope is lighter and faster and crosses the barrier more frequently than the 238U isotope.
Repeat operation thousands of times, through a succession of membranes forming a "diffusion cascade", so as to obtain uranium hexafluoride “enriched" in 235U
This method is technologically the simplest, but requires huge cascades, a lot of space and a great deal of energy.

## Slide 18: Enrichment
2. Ultracentrifuge
Enrichment process most widely used today
Use centrifugal force (centripetal accelerations) to separate 235U and 238U isotopes by taking into account their different weights.
3. Laser separation
235U atoms are ionized and separated from the (neutral) 238U by an electric field.
Reach only 3% enrichment – still on the experimental stage

## Slide 19: Enrichment depends on Fast Fission Yield
Fast fission yield, , is the number of fast-neutrons liberated per slow-neutron absorbed in the fuel (containing both 235U and 238U)
Not every absorption leads to a fission event!

## Slide 20: Why not more than 5% enrichment?
The fission yield h in the fuel – the number of (fast) neutrons produced per slow neutron absorbed – is
    1.33 for natural uranium (0.7% 235U, 99.3% 238U)
    2.00 for enriched 5% 235U, 95% 238U
2.08 for pure 235U So, not much gain from 0.7% to 100% 235U
Recall the number of fast neutrons per fission
        = 2.43 for (pure) 235U
[i.e. (2.43 – 2.08) =0.35 of the slow neutrons (ca 14%) are captured in 235U and 238U without liberation of a neutron.]

## Slide 21: Relationship between  and k
The ratio of slow neutrons resulting from fission, to the number of slow neutrons we started with is called the multiplication factor, k.
Proportional to the number of fast neutrons we get from the fission process. But we need to take into account the processes that absorb them as they collide and loose energy to become slow neutrons. So, k, k  
Number of fast neutrons initially at Nf= Ns, (  1). Ns=initial slow neutrons
  New fast neutrons resulting from fast neutron fission in 235U or 238U is Nf. ( 1)
  In a finite size reactor, lf fast neutrons leak out, so only (1-lf) survive. (lf  1)
  As neutrons slow, some absorbed resonantly in non-fission processes. Probability they don’t get lost is p. (p  1)
  Fraction of these neutrons not lost in absorptions with moderator or cladding is f
  In a finite size reactor, ls slow neutrons leak out, so only (1-ls) survive. (ls  1)
  So, number of slowed neutrons ready for the next round = Nspf(1-lf)(1-ls)
  By definition of k, this is equal to kNs
So k = pf(1-lf)(1-ls), and for infinite sized reactor, k= pf 1.11.2

## Slide 22: Fuel degradation
In operation neutrons are absorbed in both 235U and 238U.
Absorption in 238U results in heavier, transuranic, nuclei
  Occasionally neutron is exchanged for a proton
  Results in b-decay (emission of an electron or positron).
The amount of transuranic nuclei will build up, increasing the neutron absorption without fission, reducing h and k.
Fission yield:
Fast neutrons per
Slow neutron absorbed
Multiplication factor: number of slow neutrons available for new fission processes

## Slide 23: Transuranic nuclei- Actinides
Also Fissile

## Slide 24: Fuel replacement
The fuel then has to be replaced.
The fuel still contains lots of recoverable energy matter
  ~97%, in the form of U and Pu
  ~3% of waste.
Temporarily held in a storage pond while awaiting deactivation,
the spent fuel is then transported to the reprocessing plant in a sealed container called a "castle".
The spent fuel can be reprocessed.

## Slide 25: Fuel reprocessing
Separating the reusable energy matter (U and Pu) in the spent fuel from the fission products that cannot be used.
Mechanical and chemical operations
  shearing, acid dissolution, solvent separation to recover U and Pu
Recycle these mainly for the manufacture of new fuel elements (i.e. in the form of MOX – mixed oxide).
MOX is then used to fuel up to 1/3 of the reactor,
  Pu essentially replaces 235U as the fissile component.

## Slide 26: Proliferation (spreading)
Major concerns
Enrichment (development towards smaller plants make them more difficult to discover)
Nuclear reactors (if you have a reactor it is easy to make 239Pu. You only need ~10 kg 239Pu to make a bomb.)
Reprocessing (Care must be taken so that one keeps track of all the Pu produced in the reprocessing.)
Solution? International “central facilities” for handling of the fuel and waste?

## Slide 27: Life Cycle

## Slide 28: Today
Fission power plants
  Real reactors
    BWR, PWR, CANDU, HTGR
    Burners, converters and breeders
The Uranium cycle
  Nuclear fuel and replenishment
Safety
  Passive, Active, Inherent. Waste management
Accidents

## Slide 29: Safety
In case of emergency:
Passive safety
  Operates automatically without any external (human) actions or components
  (Example from everyday life: Overflow drains on bath and sinks)
Active safety
  Needs outside interference in some way
The best is to prevent the hazard from happening in the first place:
Inherent safety
  Elimination of a specific hazard by means of choice of material or concept
  (Example from everyday life: Light switches and plugs not made of conductive material and not placed in the shower enclosure)

## Slide 30: Passive safety
Part of the reactor design.
Example Worst Case Scenario: temperature rises due to loss of cooling.
A passive safety measure:
  Design reactor so that it has a negative temperature coefficient dk/dT around the operational point.
  Then reactivity goes down as temperature rises, and the temperature would presumably fall.
Another would be the use of the Doppler effect.
Will look at each

## Slide 31: Negative temperature coefficient
Assume water is used as coolant and moderator.
As coolant temperature increases some water evaporates,
  fewer water molecules left to moderate fast neutrons.
Increase in cooling water temperature  fewer slow neutrons  fewer fission processes  temperature will decrease.
If D2O is the moderator & coolant, H2O can be used to replace lost coolant to further reduce reactivity (more absorption)
Need to make sure that the core and withstand the peak temperatures encountered in this scheme

## Slide 32: The Doppler effect
Uses the fact that the probability of neutron absorption (without fission) in 238U increases with temperature
With fewer neutrons k decreases, and reactivity goes down.
This holds only when the enrichment is not too high (i.e. there must be a lot of 238U).
Most reactor types use both these measures. The Chernobyl type reactors do not use these two passive safety measures (they use graphite moderator and high enrichment factor),

## Slide 33: Safety and control rods
There is always a need for active possibilities to change the multiplication factor k, for example to start and stop a reactor.
As the fuel ages, the fission products (X and Y’s) will capture neurons without fission, and also the amount of 235U decreases.
The so-called control rods contain strongly neutron absorbing materials (like boron).
When the reactor starts, the control rods are deep in the reactor; when the fuel ages they are drawn out.
Can be inserted to stop chain reaction
  Residual heat of core remains a problem.
  Inserting control rods must not displace coolant.

## Slide 34: Inherent safety
The reactor should shut down because of physical principles, if the temperature of the core increases significantly.
When the reactor has been shut down, the decay heat of the many radioactive nuclides in the reactor should be transported away by virtue of physical principles.

## Slide 35
Process Inherent
Ultimate Safety
(PIUS)
Coolant/moderator:
water under high pressure
The reactor is embedded in
a pool of cold water with a high
concentration of boron (B).
B has a very high cross-section
for neutron absorption (sa=759 barns).
If water were to enter the reactor
core as a result from a temperature
increase, the reactor would shut
down immediately
Heat capacity of cold water enough to transport residual heat away and keep core cool

## Slide 36: Testing safety: spent fuel transport container
Two drop tests – nine-metre drop onto an unyielding surface one-metre drop onto a steel punch bar, tested at a variety of angles and under worst-case scenarios.
A fire test - the transport container is subjected to a fully engulfing liquid hydrocarbon fire for 30 minutes.
An immersion test – the transport container is subjected to immersion in water at a depth of 15 metres for eight hours for Intermediate Level Waste, or at 200 metres for one hour for High Level Waste & spent fuel.
Demonstration: a 140-tonne train travelling at 100 miles per hour was driven into a spent nuclear fuel Type B packaging. No leaks!
Ontario Hydro performed entire sequence on a single cask without leaks

## Slide 37: Testing worst case scenarios

## Slide 38: Radioactive waste
France has a major nuclear power programme
  ~1 kg of nuclear waste each year per inhabitant
  ~3,000 kg general waste (of which 100 kg is toxic).
The radioactive waste is mainly produced by nuclear power plants and fuel cycle facilities (90%).
The rest comes from the nuclear medical departments of hospitals, research laboratories and some industrial activities, such as radiographic inspection and detection, level gauges, fire alarms, etc.

## Slide 39: Management and classification principles
The classification of nuclear waste is based on two determining factors:
  its level of radioactivity and
  its lifetime
The waste is classified in three categories (A, B, C) which are each the subject of a specific management policy.

## Slide 40: Type "A" waste is of the low-level "short-lived" type
Represents 90% of all nuclear waste (gloves, protective shoe covers, protective clothing, etc.).
Compacted and conditioned in metal or concrete drums.
Drums are stored on the surface in sealed containers.
The low level of radioactivity of this waste decreases rapidly : T1/2 = 30 years
After a control period of 300 years, the radioactivity of the waste merges with natural radioactivity. The storage sites will then be considered as having achieved their "mission".

## Slide 41: Type "B" waste is of the low or medium-level "long-lived" type.
Represents slightly more than 9% of all nuclear waste.
It consists of purification resins, concentrates, filters, metal shells which contained uranium, etc.
Treated to reduce its volume, Conditioned in metal or concrete drums and stored.
One of the options envisaged for its final storage is burial in deep underground repositories.

## Slide 42: Type "C" waste is of the high-level "long-lived" type.
Represents ~0.5% of all radioactive waste
Ash from uranium combustion or fission products – These are produced by nuclear reactions in the reactor cores and recovered from spent fuel after reprocessing operations.
Its radioactivity remains high for a long period, some elements have lifetimes of thousands of years.
Several stages are involved:
  Fission products are stored in liquid form for ~5 years in stainless steel vessels where they lose part of their heat and radioactivity.
  Then vitrified by incorporation into molten glass which results in an inert material capable of containing the radioactivity. The vitrified mixture is poured into steel containers.
  These are placed in vertical metal shafts surrounded by concrete. The high radioactivity of the vitrified waste produces heat, so containers must be cooled for several years. First by air circulation and then by natural convection.
  After around thirty years they can be removed for final storage

## Slide 43: Final storage
Final storage not urgent since vitrified waste is low volume: ~3,000 m3 total volume (an Olympic swimming pool) for all type "C" waste produced in France since the beginning of the nuclear power programme (~1945) to year 2010.
Envisage underground storage at a depth of between 400 and 1,000 metres, in a favourable geological formation for long-lived radioactive waste.
Only Finland currently has long term storage facilities.

## Slide 44: Today
Fission power plants
  Real reactors
    BWR, PWR, CANDU, HTGR
    Burners, converters and breeders
The Uranium cycle
  Nuclear fuel and replenishment
Safety
  Passive, Active, Inherent. Waste management
Accidents
  INES scale, case studies

## Slide 45: Accidents INES Scale (0-7)
Fukushima Daiichi, Japan, 2011, Provisional level 7 release estimated at 10% that of Chernobyl
Fukushima Daiichi, Japan 2013—Leak of contaminated water from storage tanks during cleanup (21 Aug)
Accident prevention measures did not work
No people/Internal to plant
Outside of the facility

## Slide 46: How did the Chernobyl accident occur What they wanted to test and do:
If all other backup systems were off line and the pumps lost power, would their inertia keep enough water flow through the reactor during the 1 minute start-up time of the emergency diesel generators?
  Lower reactor output from 3.2 to 0.7 GW
    At this low level, T would be below critical with no water flow for the one minute start-up time.
  Shut off all safety backups to do this worst-case test
  Unplug the pumps and wait for the diesels to start
  Measure the water flow rate to ensure that at normal operating levels the temperatures would remain below critical.

## Slide 47: What happened?
Reduced power from 3.2 to 1.6 GW and had to stop reduction due to demand from grid
Night crew than has to complete experiment (experienced but junior)
Safeties taken off line but delay causes them to rush shutdown. Response time-constants cause the power to continue to fall from 0.7 to 0.03 GW
At these low temperature levels, contaminants coat fuel rods and absorb neutrons—slowing the reactions (like having the control rods in)
Should put control rods in to shut down and let contaminants dissipate
Instead tried to increase power to 0.7 GW to continue test
Control rods out well beyond the normal 3.2 GW operation levels, but contaminants limit output to 0.2 GW. Power slowly increases
As T increases, contaminants evaporate, power suddenly increases rapidly
At 1.4 GW, manually try to shut down reactor by inserting control rods
  Remember, all safety devices still off line!
Graphite tipped control rods displace coolant water and add graphite moderator—power jumps, graphite catches fire and remaining water boils
Last readings showed power at 33 GW as it blows. Steam at 4000 C

## Slide 48: IAEA Report September 2005
31 people died acutely, and 200 plant personnel and fire fighters suffered from acute radiation sickness.
~1,000 on-site reactor staff and emergency workers were heavily exposed to high-level radiation on the first day of the accident; among the more than 200,000 emergency and recovery operation workers exposed during the period from 1986-1987, an estimated 2,200 radiation-caused deaths can be expected during their lifetime.
The international experts have estimated that radiation could cause up to about 4,000 eventual deaths among the higher-exposed Chernobyl populations, i.e., emergency workers from 1986-1987, evacuees and residents of the most contaminated areas. This number contains both the known radiation-induced cancer and leukaemia deaths and a statistical prediction, based on estimates of the radiation doses received by these populations.
As about quarter of people die from spontaneous cancer not caused by Chernobyl radiation, the radiation-induced increase of only about 3% will be difficult to observe. However, in the most exposed cohorts of emergency and recovery operation workers some increase of particular cancer forms (e.g., leukemia) in particular time periods has already been observed.

## Slide 49: Three Mile Island Accident—What happened?
The reactor went in operation in 1978.
The accident was caused by loss of cooling water.
Because adequate cooling was not available, the nuclear fuel overheated to the point at which the zirconium cladding (the long metal tubes which hold the nuclear fuel pellets) ruptured and the fuel pellets began to melt.
It was later found that about one-half of the core melted during the early stages of the accident.
Although the TMI-2 plant suffered a severe core meltdown, the most dangerous kind of nuclear power accident, it did not produce the worst-case consequences that reactor experts had long feared.
In a worst-case accident, the melting of nuclear fuel would lead to a breach of the walls of the containment building and release massive quantities of radiation to the environment. But this did not occur as a result of the Three Mile Island accident.
For more details see:
http://www.nrc.gov/reading-rm/doc-collections/fact-sheets/3mile-isle.html

## Slide 50: Fukushima Daiichi
The individual reactors designed to withstand earthquakes with ground motion of 0.6g and a tsunami height of 5.7 m
Tohoku earthquake produced ground motion of 0.56g but a tsunami height of 8-14 m (46 to 55 minutes later) at site
Reactors automatically shut down (at ground motion 0.14g)
Tsunami caused generator power loss and cooling to units 1-3 failed
Temperatures and pressure in the cores increased
  heat from decay of fission products, not from chain reactions
Eventually hydrogen explosions at Units 1, 3 and 4, damaging or destroying portions of these reactor buildings, fuel damage suspected in Units 1, 2 and 3.
10 megacuries of radioactive iodine and cesium released,
People evacuated to avoid exposure. Of 114,488 evacuees, detectable radioactivity was found on 102 people but limited to their clothing in all cases
21 workers received doses of 10 rem, none exceeded 25 rem (the regulatory limit for emergency workers).

## Slide 51: Today
Fission power plants
  Real reactors
    BWR, PWR, CANDU, HTGR
    Burners, converters and breeders
The Uranium cycle
  Nuclear fuel and replenishment
Safety
  Passive, Active, Inherent. Waste management
Accidents
  INES scale, case studies

## Slide 52: Next time
Radiation and health
Fusion
Start on bio-fuel