## Slide 1: Nuclear Energy 3 Accidents and Fusion
<number>
Boeker & Grondelle Chap. 5
6 September 2013
Notes: <number>

## Slide 2: Last Time
<number>
Fission power plants
  Real reactors
    BWR, PWR, CANDU, HTGR
    Burners, converters and breeders
The Uranium cycle
  Nuclear fuel and replenishment
Safety
  Passive, Active, Inherent. Waste management
Accidents
  INES scale
Notes: <number>

## Slide 3: Today
<number>
Accidents
  Top 3, basic meltdowns
Radiation and health
Fusion
Bio mass and Bio Fuels
Notes: <number>

## Slide 4: Accidents INES Scale (0-7)
<number>
Fukushima Daiichi, Japan, 2011, Provisional level 7 release estimated at 10% that of Chernobyl
Fukushima Daiichi, Japan 2013—Leak of contaminated water from storage tanks during cleanup (21 Aug)
Accident prevention measures did not work
No people/Internal to plant
People, or environment external to facility

## Slide 5: How did the Chernobyl accident occur What they wanted to test and do:
<number>
If all other backup systems were off line and the pumps lost power, would their inertia keep enough water flow through the reactor during the 1 minute start-up time of the emergency diesel generators?
  Lower reactor output from 3.2 to 0.7 GW
    At this low level, T would be below critical with no water flow for the one minute start-up time.
  Shut off all safety backups to do this worst-case test
  Unplug the pumps and wait for the diesels to start
  Measure the water flow rate to ensure that at normal operating levels the temperatures would remain below critical.
Notes: <number>

## Slide 6: What happened?
<number>
Reduced power from 3.2 to 1.6 GW and had to stop reduction due to demand from grid
Night crew than has to complete experiment (experienced but junior)
Safeties taken off line but delay causes them to rush shutdown. Response time-constants cause the power to continue to fall from 0.7 to 0.03 GW
At these low temperature levels, contaminants coat fuel rods and absorb neutrons—slowing the reactions (like having the control rods in)
Should put control rods in to shut down and let contaminants dissipate
Instead tried to increase power to 0.7 GW to continue test
Control rods out well beyond the normal 3.2 GW operation levels, but contaminants limit output to 0.2 GW. Power slowly increases
As T increases, contaminants evaporate, power suddenly increases rapidly
At 1.4 GW, manually try to shut down reactor by inserting control rods
  Remember, all safety devices still off line!
Graphite tipped control rods displace coolant water and add graphite moderator—power jumps, graphite catches fire and remaining water boils
Last readings showed power at 33 GW as it blows. Steam at 4000 C
Notes: <number>

## Slide 7: IAEA Report September 2005
<number>
31 people died acutely, and 200 plant personnel and fire fighters suffered from acute radiation sickness.
~1,000 on-site reactor staff and emergency workers were heavily exposed to high-level radiation on the first day of the accident; among the more than 200,000 emergency and recovery operation workers exposed during the period from 1986-1987, an estimated 2,200 radiation-caused deaths can be expected during their lifetime.
The international experts have estimated that radiation could cause up to about 4,000 eventual deaths among the higher-exposed Chernobyl populations, i.e., emergency workers from 1986-1987, evacuees and residents of the most contaminated areas. This number contains both the known radiation-induced cancer and leukaemia deaths and a statistical prediction, based on estimates of the radiation doses received by these populations.
As about quarter of people die from spontaneous cancer not caused by Chernobyl radiation, the radiation-induced increase of only about 3% will be difficult to observe. However, in the most exposed cohorts of emergency and recovery operation workers some increase of particular cancer forms (e.g., leukemia) in particular time periods has already been observed.
Notes: <number>

## Slide 8: Three Mile Island Accident—What happened?
<number>
The reactor went in operation in 1978.
The accident was caused by loss of cooling water.
Because adequate cooling was not available, the nuclear fuel overheated to the point at which the zirconium cladding (the long metal tubes which hold the nuclear fuel pellets) ruptured and the fuel pellets began to melt.
It was later found that about one-half of the core melted during the early stages of the accident.
Although the TMI-2 plant suffered a severe core meltdown, the most dangerous kind of nuclear power accident, it did not produce the worst-case consequences that reactor experts had long feared.
In a worst-case accident, the melting of nuclear fuel would lead to a breach of the walls of the containment building and release massive quantities of radiation to the environment. But this did not occur as a result of the Three Mile Island accident.
For more details see:
http://www.nrc.gov/reading-rm/doc-collections/fact-sheets/3mile-isle.html
Notes: <number>

## Slide 9: Fukushima Daiichi
The individual reactors designed to withstand earthquakes with ground motion of 0.6g and a tsunami height of 5.7 m
Tohoku earthquake produced ground motion of 0.56g but a tsunami height of 8-14 m (46 to 55 minutes later) at site
Reactors automatically shut down (at ground motion 0.14g)
Tsunami caused generator power loss and cooling to units 1-3 failed
Temperatures and pressure in the cores increased
  heat from decay of fission products, not from chain reactions
Eventually hydrogen explosions at Units 1, 3 and 4, damaging or destroying portions of these reactor buildings, fuel damage suspected in Units 1, 2 and 3.
10 megacuries of radioactive iodine and cesium released,
People evacuated to avoid exposure. Of 114,488 evacuees, detectable radioactivity was found on 102 people but limited to their clothing in all cases
21 workers received doses of 10 rem, none exceeded 25 rem (the regulatory limit for emergency workers).
<number>

## Slide 10: Today
<number>
Accidents
  Top 5, basic meltdowns, INES scales
Radiation and health
  Definition of Sievert, “Safe” dosages
  Quality factor determined by effect of radiation on cells in a Petrie dish (no account for skin absorption).
Fusion
Notes: <number>

## Slide 11: Radiation doses
<number>
Measured in grays (Gy), the absorption of 1J energy per kg of body mass.
1 Gy=1 J/kg
Heavy particles of high energy do much more damage than lighter particles of low energy when they dispose the same amount of energy into the living tissue.
Therefore the dose in gray is multiplied by a quality factor Q, resulting in a new unit sievert Sv.
The quality factor is in part determined experimentally and in part based on expert judgment. Indicates what dose of X rays or gamma rays would produce the same amount of damage of biological damage in a human being—”dose equivalent”
1 Sv=QJ/kg (since Q is unit-less) The amount of any kind of radiation which would cause the same amount of biological damage in a human being as absorbing 1 Gy of X rays
Notes: <number>

## Slide 12
<number>
& E >20 MeV
100 keV < E < 2 MeV
Note: Measured for radiation incident on cells.
    For -particles, Q is only meaningful for internally deposited emitters as they cannot traverse the layer of dead skin that surrounds people.
Notes: <number>

## Slide 13: Background radiation
<number>
Natural sources: 2 mSv/year
Medical applications: 2 mSv/year
What is a safe dose? How much can we accept from other sources?
Note: The Sievert is intended to be used at the sort of radiation levels encountered in medicine or the workplace; it “should not be used in assessing the effects of high-level, accidental exposures.”
    International Commission on Radiation Units, ICRU
Notes: <number>

## Slide 14
<number>
If the dose is 200 mSv a human will experience a temporary decrease of white blood cells.
For 2000 mSv the resistance against infections will be gone.
At 5000 mSv nausea and diarrhoea will be acute with death within a few months.
A dose of 80 000 mSv is lethal within a few hours.
Three-Mile Island: one person received 0.8 mSv
Chernobyl: 135 000 people received 100 mSv
Fukushima Daiichi: 210 000 residents received < 1mSv (one plant worker got 670 mSv on feet)
Notes: <number>

## Slide 15: Today
<number>
Accidents
  Top 5, basic meltdowns, INES scales
Radiation and health
  Definition of Sievert, “Safe” dosages
  Quality factor determined by effect of radiation on cells in a Petrie dish (no account for skin absorption).
Fusion
  Basic reaction for fusion: 2D + 3T → 4He + n + 17.6MeV
  Fuel (D2O from seawater, T from neutron bombardment of Li)
  Tokamak (heating a magnetically confined plasma) and Laser fusion (radiation pressure heats and confines plasma)
  Lawson Criterion for fusion
Notes: <number>

## Slide 16
<number>
Fusion power plants
  The fusion reaction
  How to achieve fusion
  When do you know you have reached it!
Notes: <number>

## Slide 17: Fusion
<number>
Reactions that are possible in practice
Hydrogen (Z=1, A=2,3) nuclei fusion to form helium (Z=2, A=4) nuclei.
Fission
Fusion
Fission
Fusion
Notes: <number>

## Slide 18: Fusion Plant in the Sky: The Sun
<number>
Two pairs of protons fuse, forming two deuterons (an H atom nucleus).
Each deuteron fuses with an additional proton to form helium-3.
The two helium-3 nuclei fuse to create beryllium-6, which is unstable and disintegrates into two protons plus a helium-4 (alpha particle).
The process also releases two neutrinos, two positrons, and gamma rays.
The positrons annihilate quickly with electrons in the plasma, releasing additional energy in the form of gamma rays. The neutrinos interact so weakly that they immediately exit the sun.
The P-P reaction-18.3 MeV
Neutron
Proton
Notes: <number>

## Slide 19: Fusion on the Ground
<number>
Hydrogen isotopes:
Neutron
Proton
Temp=108 K = 20 keV
Notes: <number>

## Slide 20: Fusion of hydrogen nuclei
<number>
2D + 3T → 4He + n + 17.6MeV
(Z=1, N=1) + (Z=1, N=2) → (Z=2, N=2) + (N=1)
ZLeft=2, NL=3 ZRight=2, NR=3
Other reactions possible:
2D + 2D → 3He + n + 3.27MeV
2D + 2D → 3T + 1H + 4.03MeV
2D + 3He → 4He + 1H + 18.3MeV
Favoured for 1st genreration fusion reactors
Notes: <number>

## Slide 21: What are the challenges in fusion of hydrogen nuclei?
<number>
The positively charged nuclei must overcome the Coulomb repulsion (500-600 keV), before the attractive nuclear forces can lead to fusion.
But due to tunnelling through the Coulomb barrier, only 0.1 MeV is needed for 2D and 3T fusion. Reaction maximizes at 40 keV.
How can this energy be supplied to the nuclei?
  Electromagnetic Waves
  Ohmic Heating (by electric currents)
  Collisions with neutral Particle Beams (atomic hydrogen)
  Compression (by magnetic fields) .
The temperature needed amounts to 108K (or T=20 keV. At these temperatures a large fraction of the nuclei have the energy needed).
At these temperatures the hydrogen (D/T) atoms will be ionized, forming a plasma: a neutral mixture of the positively charged nuclei and the “free” electrons.
Notes: <number>

## Slide 22: Fusion fuel
<number>
We need tritium and deuterium.
Is that found in nature?
No and yes:
  Tritium has a half-life of 12.3 years, so not much of it around, but it can be formed by bombarding lithium Li (which there is a lot of) with neutrons (which are produced in D-T fusion reaction)
  One out of 6700 hydrogen atoms in water is deuterium, that can be extracted by repeated hydrolysis.
Notes: <number>

## Slide 23: Fusion reactors
<number>
The ions and the electrons in the plasma must be prevented from hitting the walls of the reactor, otherwise so many alien nuclei would be sputtered from the walls that a fusion reaction would stop immediately.
How can you contain a plasma without using walls?
Solution: use magnetic fields.
Notes: <number>

## Slide 24: Tokamak
<number>
From the Russian words for
To= toroidal
Ka=chamber
Mak= magnetic
Notes: <number>

## Slide 25: D-T fusion reactor
<number>
d = deuterium
t = tritium
Notes: <number>

## Slide 26: D-T fusion power plant
<number>
Notes: <number>

## Slide 27: Laser fusion reactor
<number>
move the heat energy. The tritium produced in the lithium mantle is
separated out and incorporated into new D-T pellets.
NOVA-laser at Lawrence Livermore Laboratory, Univ. of California
Now building the National Ignition Laboratory
Notes: <number>

## Slide 28: Energy output
<number>
It takes a lot of energy to heat and sustain the plasma.
To have a net energy output, the energy “produced” (converted) in the fusion process must be larger than the losses plus the energy needed to sustain the plasma.
Japan Atomic Energy Research Institute (JAERI)
JapanTokamak-60 (JT-60)
Reached an equivalent fusion power gain of 1.25 (briefly-28.6 sec)
Notes: <number>

## Slide 29: Conventional Fusion FAQ Glossary http://www.faqs.org/faqs/fusion-faq/glossary/
<number>
Ignition: In fusion, as in an ordinary (chemical) fire, ignition is the point where the temperature and confinement of heat in the fuel (plasma in the case of fusion) are such that energy released from ongoing reactions is sufficient to maintain the temperature of the system, and no external heating is needed. An ignited fusion plasma produces so much energy from fusion reactions that the plasma is fully heated by fusion reaction products (alpha particles in the case of D-T fusion), and the plasma no longer needs any external source of power to maintain its temperature. (The plasma may, however, still need something to maintain its confinement; this gives us control over the fusion reaction and helps prevent fusion reactors from having "meltdown" problems like fission reactors.)
Poisoning: Buildup of ash and impurities in a fusion plasma tends to reduce the quality of the plasma and reduce the fusion output; this sort of process is sometimes called "poisioning" the reactor or the plasma. See also ash, impurities.
Impurities: atoms of unwanted elements in the plasma, which tend to degrade plasma performance, and in the case of fusion plasmas tends to inhibit fusion ("poisoning the reactor").
Notes: <number>

## Slide 30
<number>
Instability: A state of a plasma (or any other physical system) in which a small perturbation amplifies itself to a considerable alteration of the state of the system. In plasmas instabilities sometimes leads to disruptions (see entry). Most instabilities are associated with waves and other natural modes of oscillation in the plasma, which can sometimes grow. There are (unfortunately!) many kinds. See also: Flute instability, MHD instability, Interchange instability, microinstability, kink instability, resistive instability, trapped particle instability, two-stream instability, universal instability, and velocity-space instability
Disruption: Plasma instabilities (usually oscillatory modes) sometimes grow and cause disruptions of the carefully-engineered plasma conditions in the reactor. Major disruptions can cause an abrupt temperature drop and the termination of the plasma. Stored energy in the plasma is rapidly dumped into the rest of the plasma system (vacuum vessel walls, magnet coils, etc.) and can cause significant damage if precautions are not taken.
Notes: <number>

## Slide 31: Lawson criterion
<number>
Radiation & thermal power lost by plasma
Power leaving the plasma
Criterion for energy gain:
PT > PH=PL
That is:
PTh > (1-PL/
=fraction of PT recovered
Radiation & thermal power lost by plasma
Or:
(Pth + PL) > PL
Notes: <number>

## Slide 32: Energy loss and gain in the plasma
<number>
Consider a unit volume of plasma that will be confined for a finite time E.
The lifetime of the plasma is determined
  by instabilities,
  by the fractions of ions that hit the walls,
  by collisions between ions and electrons, and
  by the synchrotron radiation originating from the helix-circular shape of the particle orbits.
Estimate the terms in the Lawson equation to see what sort of plasma densities and confinement times we need.
Notes: <number>

## Slide 33: Loss of thermal energy in the plasma
<number>
If there are n ions and n electrons per m3, the energy per m3 is
  2 n x 3/2kT = 3nkT
If the lifetime of the plasma is E, and all the thermal energy is lost during this time, then the loss per second is
3nkT/E
According to the equipartition theorem, it is possible to define thermal energy. In a system of N molecules, each with f degrees of freedom, and if there are no other (non-quadratic) temperature-dependent forms of energy, then the total thermal energy of the system is Uthermal= Nf kT/2
Notes: <number>

## Slide 34: Bremsstrahlung
<number>
When charged particles meet, energy is lost through emission of Bremsstrahlung radiation (deceleration radiation).
The number of encounters will be proportional to
n(n-1)n2, and
the number of encounters will be proportional to the relative velocity of the particles.
The relative velocity will on average depend on the square root of the kinetic energy, i.e (kT)½.
The Bremsstrahlung loss per second can therefore be written:
n2 (kT)½, where  is a constant.
Notes: <number>

## Slide 35: Total loss
<number>
The total energy loss per second in the plasma can therefore be expressed as
  PL = n2 (kT)½ + 3nkT/E.
Notes: <number>

## Slide 36: Power generation – the number of reactions
<number>
Assume we have nd deuterium and nt tritium atoms per m3, and that the tritium atoms have a velocity u with respect to the deuterium.
The number of fusion reactions per deuterium nuclei per second is nt u ,
where  is the cross-section of the reaction.
The total number of reactions per second and per m3 can be expressed as
R = nd nt <u>,
where <u> is averaged over all u combinations.
Notes: <number>

## Slide 37: Total “power production”
<number>
The total (thermonuclear) power production Pth is the number of reactions per second R multiplied by the energy produced per fusion E (17.6 MeV for the D+T fusion).
For simplicity we take nt=nd=n/2, then
  Pth = R x E = nd nt <u> x E
  = n2/4 <u> E
The break-even point for the production of fusion power, would be reached when the energy production becomes larger than the energy loss.
Notes: <number>

## Slide 38
<number>
PT = Pth + PL = n2/4 <u> E + n2 (kT)½ + 3nkT/E
Criterion for energy gain:
PT =(Pth + PL) > PL
Notes: <number>

## Slide 39: Lawson criterion equation
<number>
Criterion for energy gain: PT =(Pth + PL) > PL
This can be rewritten
Pth > (1-)PL
and we can insert for Pth (= n2/4 <u> E) and
PL (= n2 (kT)½ + 3nkT/E) and solve for nE:
i.e. at about kT25keV, the right hand side of the equation is a minimum, and the product of density n and the lifetime E of the
plasma has the best chance of being > right hand side
(Eq 4.282)
Notes: <number>

## Slide 40
<number>
Lawson diagram Q = Energyout/Energyin
external heating not needed
energy out  in
Note: unit neT
2016+?
Notes: <number>

## Slide 41
<number>
ITER Next generation fusion reactor
A joint international R/D development project to demonstrate the scientific and technical feasibility of fusion power.
  EU
  Japan
  People´s Republic of China
  India
  Republic of Korea
  the Russian Federation
  USA.
http://www.iter.org/
Notes: <number>

## Slide 42: Today
<number>
Accidents
  Top 5, basic meltdowns, INES scales
Radiation and health
  Definition of Sievert, “Safe” dosages
  Quality factor determined by effect of radiation on cells in a Petrie dish (no account for skin absorption).
Fusion
  Basic reaction for fusion: 2D + 3T → 4He + n + 17.6MeV
  Fuel (D2O from seawater, T from neutron bombardment of Li)
  Tokamak (heating a magnetically confined plasma) and Laser fusion (radiation pressure heats and confines plasma)
  Lawson Criterion for fusion
Notes: <number>