## Slide 1: Conventional energy finish Nuclear Energy Introduction
<number>
Boeker & Grondelle Chap. 4
Boeker & Grondelle Chap. 5
30 August 2013
Notes: <number>

## Slide 2: Last time
<number>
Heat engines
  The internal combustion engine, Steam engines, the Stirling engine- cycles, work & efficiency
  Electricity generation via Steam turbines, Gas turbines- how they work, typical overall efficiency
  Combined system efficiency-how to calculate
Pollution and pollution management-CO, CO2, NOx, SOx, VOC and Particles: their major sources and health effects
  Electric generators (dynamos)-Basic Principle and load distribution on grid
Notes: <number>

## Slide 3: Today’s Topics
<number>
Transport of electric energy
Energy storage
Nuclear Power
Notes: <number>

## Slide 4: Electric Energy transport
<number>
Transport of electric energy
Transported as current (either AC or DC)
Ohmic losses are the most important: Plost = I2R
Total power sent along the power line: PT = VI
The ratio of power lost to power transported:
This ratio should be as small as possible
  Reduce R (thicker wire → expensive, or use superconductor R=0)
  Increase V (typically 380 000V)
Notes: <number>

## Slide 5: Power lines and health effects
<number>
Alternating currents in the wires induce alternating magnetic fields that may be harmful, by inducing currents in the human body (and other conductive objects).
In most cases the currents produced by the body itself (in the brain and to keep the heart going) are larger.
But still there are no firm conclusions on the health risks connected to being close to power lines.
Need more research on the effect of electromagnetic radiation, not only for power lines, but also for e.g. mobile phones.
Power transported as Phased power to reduce radiated power (i.e. 3 phase)
Notes: <number>

## Slide 6
<number>
Capacitive coupling with high-voltage power lines can light a lamp continuously at low intensity--Wikipedia
Is this your brain on EMF?
http://www.treehugger.com/files/2008/02/emf_richard_box.php
Notes: <number>

## Slide 7: Overview
<number>
Transport of electric energy
Energy storage
Nuclear Energy
Notes: <number>

## Slide 8: Energy storage
<number>
Energy is not always converted when it is needed:
it needs to be stored –particularly true for renewables
  Gravitational storage (mgh—hydropower)
  Flywheels (½ mr22)
  Batteries
  Hydrogen
  Fuel
Amount of available energy per weight
Rate at which available energy can be taken per weight
Notes: <number>

## Slide 9
<number>
J/kg
Notes: <number>

## Slide 10: Comparisons
<number>
Assume a power plant has produced 500 MWe during 6 hours (in the night), which has to be stored in some way.
In joules this correspond to …
1W = 1J/s → 1J = 1Ws (must multiply by the number of seconds the power is delivered)
500 x 106 (J/s) x 6 (h) x 3600 (s/h) = 1.08 x 1013 (Ws =J)
Water pumping (100m): ~103J/kg → we need to pump 1010kg water (107m3)
H2: ~105kJ/kg = 108J/kg → we need 105kg H2 (a lot but not impossible, but fuel cells that convert from H2 to electricity are still expensive)
The hydrogen is produced by electrolysis of water
2H2O + electric energy → 2H2 + O2
Notes: <number>

## Slide 11: Overview
<number>
Pollution
  CO, CO2, NOx, SOx, VOC and Particles: their major effects
Electric generators (dynamos)
  Basic Principle and load distribution on grid
Transport of electric energy
  Power Loss
Energy storage
  Specific Energy vs. Specific Power
  Highest to lowest Specific Energy: Fuels, Batteries & Flywheels, Hydro-storage, Capacitors
Notes: <number>

## Slide 12: B&G Chap 5: Nuclear energy – part 1 30 August 2013
<number>
Notes: <number>

## Slide 13: Topics for Today in Nuclear Power
<number>
The basis for nuclear power
Basic principles of fission
Chain reactions
Control
Fission power plants
Notes: <number>

## Slide 14: The basis for nuclear power
<number>
Nucleus:
  Number of Protons (+ charge), Z (= Atomic Number)
    Mass of proton : 1,6726 x 10-27kg (~2000 x that of electron)
  Number of Neutrons, N
    Mass of neutron : 1,6749 x 10-27kg (> mass of proton)
  Total number of Nucleons, A = Z+N (=Atomic Mass, g/mole)
  Example:
         decay 
        - decay 
        + decay 
         decay  Nucleus de-excites and give off photon
neutronproton+energy
proton+energyneutron
emit -particle= 4He + energy
 Means gets converted to
Notes: <number>

## Slide 15: Radioactive Decay— Decay
<number>
A  ray is a high energy photon.
Like visible photons,  rays can be emitted when a nucleus undergoes a transition from one such configuration to another. E.g. when the shape of the nucleus undergoes a change.
Neither the mass number nor the atomic number is changed when a nucleus emits a  ray in the reaction
Notes: <number>

## Slide 16
<number>
=positron
=electromagnetic radiation
1
1
?
?
?
?
Notes: <number>

## Slide 17: Half life
<number>
The time dependence of the (spontaneous) decay of a radioactive nucleus follows
  N(t) = N0 exp(-t / )
  where N0 represents the number of nuclei at time t=0 and  is the decay constant.
The half-life t½ is the time when the number of nuclei is reduced to N0/2
Notes: <number>

## Slide 18: Half life examples
<number>
Element | Isotope | Half-life T½
Uranium | 238U | 4 500 000 000 years
Uranium | 235U | 700 000 000 years
Plutonium | 239Pu | 24 000 years
Caesium | 137Cs | 30 years
Hydrogen | 3H (tritium) | 12.4 years
Strontium | 89Sr | 50.5 days
The earth was formed 5 000 000 000 years ago
Notes: <number>

## Slide 19: Binding Energy
<number>
To separate the particles in the nucleus (nucleons), they must be pulled apart against the attractive strong force.
  Like separating magnets!
  They have potential energy when they are separated.
  When the particles come together to form a nucleus, their potential energy decreases (liberates energy).
  Energy must be put in to separate the nucleons of a nucleus
Binding Energy
  Not the energy needed to bind them together
  Energy needed to break the bonds (and therefore the Energy released when bonds are formed)
Notes: <number>

## Slide 20: Binding Energy
<number>
Binding energy is a function of Mass Number
A=56 (Iron) is a peak (Fe is the most stable element)
Thus in decay process:
  Very heavy nuclei (A>>56) decay into lighter ones (A>56)
  Very light nuclei (A<<56) decay into heavier ones (A<56),
Binding energy per nucleon increases (Release Energy)
Energy will be released in the processes, E= mc2.
Fission break a heavy one apart to form 1 or more lighter ones
Fusion smush very light ones together to form a heavier one
Notes: <number>

## Slide 21: Example
<number>
236A  118B + 118B
Takes this much energy to break 236A apart
Get this out for each 118B formed
More out than in!
236*7.6 MeV IN 1793.6 MeV in
2x(118*8.4 MeV) OUT 1982.4 Mev out
Liberate:
OUT-IN = 188.8 MeV
Or 0.8 MeV/Nucleon
Notes: <number>

## Slide 22: Fission
<number>
Fission is a nuclear process in which a heavy nucleus is split into smaller nuclei.
Can be Spontaneous Fission
  Some heavy nuclei decay spontaneously into smaller nuclei
Can be Induced Fission
  Nucleus is bombarded by a neutron and splits into smaller nuclei
Both processes generally release neutrons and energy
Notes: <number>

## Slide 23: Fission
<number>
Most nuclear power plants today are based on induced fission of 235U by absorption of a low energy neutron
Why is 235U used instead of 238U?
Thermal neutrons are neutrons in thermal equilibrium with the surrounding matter (E=kT0.025 eV at room temperature)
Fission cross-section for
thermal (slow) neutrons,
i.e. fission probability.
Notes: <number>

## Slide 24: Why Low Energy: Fission probability
<number>
Notes: <number>

## Slide 25: Fission Process of 235U
<number>
Z (92 each side) : 92 (U) → 56 (Ba) + 36 (Kr)
N (144 each side): 1 (n) + 143 (U) → 3 (n) + 88 (Ba) + 53 (Kr)
87
54
(Many other
products
are possible)
Heat & Energy
Notes: <number>

## Slide 26: Where does the released energy come from?
<number>
Notes: <number>

## Slide 27: Energy gain
<number>
Binding energy per nucleon:
  0 MeV for neutrons
  7.59 MeV for 236U (Energy IN)
  8.62 MeV for 89Kr (Energy OUT)
  8.27 MeV for 144Ba (Energy OUT)
Total binding energy for
236U: (236 x 7.59)MeV = 1791 MeV
89Kr: ( 89 x 8.62)MeV = 767 MeV
144Ba: (144 x 8.27)MeV = 1191 MeV
Kinetic Energy gained by products in the fission process:
  (767 + 1191 – 1791 ) MeV = 167 MeV
Notes: <number>

## Slide 28: Total Energy Budget
<number>
Form of Energy Released | Energy Released (MeV)
Kinetic energy of two fission fragments | 168
Immediate gamma rays | 7
Delayed gamma rays | 3-12
Neutrons | 5
Energy of decay products of fission fragments (e.g. 144Ba and 89Kr can themselves decay) | ...
Gamma rays | 7
Beta particles | 8
Neutrons | 12
Average total energy released per fission: | ~215 MeV
The neutrons and the fission products share that energy as kinetic energy, collide with the surrounding material and loose that kinetic energy as heat to the surroundings (165-170 MeV).
Notes: <number>

## Slide 29: Compared to photosynthesis
<number>
In photosynthesis 29 eV is stored when carbohydrate is formed:
6CO2+6H2O+29eV→C6H12O6+6O2
How much is stored per nucleon?
C: Z+N =14, H: Z+N = 1 O: Z+N = 16
29 / (6x14 + 12x1 + 6x16) eV/nucleon = 29/192 eV/nucleon = 0.15 eV/nucleon.
This molecular binding energy of the carbohydrate is released when the biomass (or hydrocarbons) is combusted.
In fission of 235U, ~200 MeV is released
The nuclear binding energy per nucleon is ~ 8 MeV,
i.e 107 times more than what is stored in biomass.
Notes: <number>

## Slide 30: Nuclear (fission) power stations
<number>
Typically 235U is used as a fuel (natural or enriched uranium)
Basic reaction:
Start the reaction with a few external neutrons
Maintain a chain reaction, with the product neutrons
  this keeps reaction going while producing energy.
The energy liberated in the fission processes is converted to heat, which drives a heat engine, usually based on steam.
Notes: <number>

## Slide 31: Self-Sustaining or Chain Reaction
<number>
Note that we get more neutrons out of the 235U reaction than we put in:
Similar to a catalytic reaction in chemistry
Those extra neutrons can cause other 235U nuclei to decay
X
Y
~5Mev
Notes: <number>

## Slide 32: But Fission probability small for 5 MeV neutrons
<number>
Notes: <number>

## Slide 33: How can the fission cross-section be increased? Moderators
<number>
Slow down the fast (5 MeV) neutrons
  Need to reach thermal energies (0.025 eV)
  Do not want them all lost to absorption.
In a moderator (usually water) a neutron at high speed hits a proton at rest.
Since the proton and the neutron have similar mass, the neutron looses half its kinetic energy in the collision.
After many collisions the neutrons reach thermal energies where the fission cross-section is high.
Notes: <number>

## Slide 34: Sustainable Chain Reaction
<number>
If all 2.43 neutrons went off to initiate new fission events the energy released grow rapidly!
  Good in a bomb. Less desirable in a nuclear power plant
Fortunately during the slow-down process the neutrons can be absorbed in the moderator, in the 238U or in the reactor vessel
The number of liberated neutrons per fission event (2.43) is reduced to the so-called multiplication factor k.
Notes: <number>

## Slide 35: Neutron escape and reactor size
<number>
If the reactor is of infinite size, no neutrons will be lost to the outside.
In this case the multiplication factor is called k∞, and it is always larger than k for a real sized reactor.
For a typical reactor k∞ is in the order of 1.10 to 1.20 (still a bomb!)
Consider a spherical reactor with k  k∞, and let the size decrease until at a certain stage k=1 (1 neutron in, only one out for next event)
This, k=1, is the critical size of the reactor. If the reactor is larger than the critical size, the chain reaction will be unstable.
A different shape would have a surface/volume ratio larger than that of a sphere, so more neutrons lost at the surface (k will be < ksphere). Thus the reactor could be enlarged before reaching critical size (hold more fuel).
Generally, non-spherical shapes safer to work with than spherical.
Notes: <number>

## Slide 36: Steady-state operation
<number>
For steady state operation, we want k=1, so k∞ must be larger than 1 (since k< k∞).
The maximum value for k∞ is , the number of fast neutrons liberated in each fission process.
Remember that on average=2.43, so we can not afford to loose to many neutrons in the moderation process.
In a reactor using natural uranium, there is only 0.7% 235U, so neutrons hit 238U more often and can be absorbed.
If the reactor is also using ordinary water H2O as a moderator, many neutrons are absorbed,
So with ordinary uranium in water, k∞ is only 1.1
Not much to work with in reactor design
Notes: <number>

## Slide 37: Solutions
<number>
Enrich the uranium, to about 2.5% 235U and/or
Use “heavy water” D2O as moderator that absorb fewer neutrons while has more stopping power than .
To maintain k=1, control rods that absorb the excess neutrons (k∞1), are used in the reactor.
T steam ~300oC
So   34% (Carnot)
Notes: <number>

## Slide 38: The ”life and death” of neutrons in U fission reactors
<number>
Start with 1 slow (thermal) neutron, go via  fast neutrons, end up with k slow ones:
Steady-state: k=1 (< k∞)
one new slow neutron per incoming slow neutron
Notes: <number>

## Slide 39: Vocabulary: Fissionable and fissile isotopes
<number>
Many heavy elements, such as uranium, thorium, and plutonium, undergo both spontaneous fission (radioactive decay) and induced fission (a nuclear reaction).
Isotopes that undergo induced fission when struck by a free neutron are called fissionable;
Isotopes that can sustain a chain reaction (at least one neutron is a product) are also called fissile (i.e. not all fissionable isotopes are fissile).
A few particularly fissile and readily obtainable isotopes (notably 235U and 239Pu) are called nuclear fuels because they can sustain a chain reaction and can be obtained in large enough quantities to be useful.
238U is fissionable (with fast neutrons), but not fissile.
Notes: <number>

## Slide 40: Time dependence and control
<number>
In a reactor a neutron reproduces itself in a time L:
  The neutrons will first slow down by collisions and then stay for some time with thermal energies in the moderator, before they are absorbed by the 235U of one of the fuel rods.
  Then the neutrons immediately cause another fission.
L is typically 10-4 s
Notes: <number>

## Slide 41: A disturbance from steady-state
<number>
Assume that k increases from k=1 to k=1+
Then during a time interval dt=L, the number of neutrons have increased from N to kN = (1+)N, or from N to N+dN, giving dN=N.
One can express this as a differential:
  dN/dt = N/L
that can be integrated to give:
N(t) = N0 exp(t/L) = N0 exp(t/)
where =L/ is the time constant of the process.
Notes: <number>

## Slide 42: A numerical example
<number>
Let the disturbance be small; =10-3
Then with L=10-4 s, the time constant becomes =0.1 s.
This means that after 10 seconds (t=10s)
N(10) = N0 exp(10/0.1) = N0 exp(100) = 1043 N0 (!!)
During these 10 seconds the amount of liberated energy has increased by the same 1043 factor, and a melt down, chemical explosions and possibly a blow-up of the container would have occurred.
Thus time constants of =0.1 s gives very little reaction time for counter measures.
How can we still have reasonably controllable reactors?
Doooo!
Notes: <number>

## Slide 43: Delayed neutrons
<number>
There was a mistake in the presented calculation:
Not all neutrons are liberated immediately in the fission process.
A small fraction=0.0065 result from the decay of the fission products X and Y and their “daughters”, and are called delayed neutrons.
On average the delay time td=9s.
Including the delay time the reproduction time becomes L*=(1-)L + td  td  0.05 s (indeed, this is >> L=10-4s).
Then the time constant becomes= L*/= 50 s, which is long enough to take mechanical counter measures, such as pushing in the neutron absorbing control rods.
Mmmm
Doughnuts
Notes: <number>

## Slide 44
<number>
This means that after 10 seconds (with a time constant of = 50 s):
N(10) = N0 exp(10/50) = N0 exp(0.5) = 1.6 N0
The number of neutrons will have increased by a factor 10 after a time t10, that is found from
10N0 = N0 exp(t10/50) → ln(10)=t10/50 → t10 =50ln(10) = 115 s
and by a factor 100 after a time t100, that is found from
100N0 = N0 exp(t100/50) → ln(100)=t100/50 → t100 =50ln(100) = 230 s
IF  is very large ( > ), then the time constant shortens to the point where we the prompt neutrons are back in control. =0.59*=0.1 s
Notes: <number>

## Slide 45: Overview
<number>
The basis for nuclear power
Basic principles of fission
Chain reactions
Control
Fission power plants
  Real reactors
    BWR, PWR, CANDU, HTGR
    Burners, converters and breeders
Notes: <number>

## Slide 46: The various nuclear systems
<number>
Not all nuclear power plants are the same.
There are various systems which are characterised by three basic
elements:
fuel: enriched or natural uranium; plutonium, thorium (rarely used).
moderator: ordinary water; heavy water; graphite.
heat exchanger fluid: ordinary water either pressurised or boiling; heavy water; carbon dioxide; sodium; helium.
The pressurized water reactor (PWR) is the most widely used reactor
system in the world.
Notes: <number>

## Slide 47: Pressurised water reactor
<number>
Higher pressure: higher boiling point: warmer water (320C @150 bar)
Efficiency : 34%
Notes: <number>

## Slide 48: Boiling water reactor
<number>
Efficiency: 33%
Notes: <number>

## Slide 49
<number>
From the Institution of Engineering and Technology
Notes: <number>

## Slide 50: Burners, converters and breeders
<number>
Reactors such as BWR and PWR are called converters: They produce 233Th and 239Pu which could be used to run reactors from the reaction of FAST neutrons.
That is, 233Th and 239Pu are fissile with fast neutrons
Conversion Ratio = (fissile material produced) / (fuel burned) is used to classify reactors.
If the conversion ratio is 0 the reactor is a burner, if it is between 0 and 1 it is a converter and if it is larger than 1 it is a breeder.
Notes: <number>

## Slide 51: Breeders
<number>
The breeder produces more fuel than it burns.
In a breeder extra 238U is put into the reactor core, to make 239Pu.
In a fast breeder reactor (FBR), the chain reaction is sustained by fast neutrons (no need for moderator).
Breeders and bombs
A critical mass is the minimum amount of fissile material that can sustain a chain reaction internally (and therefore explode).
Pu has a smaller critical mass than U, so it takes less material to make a bomb.
Notes: <number>

## Slide 52: Breeder advantages and disadvantages
<number>
+ Breeder power plants might not run out of fuel in 50 000 years
+ With sea water extraction of Uranium, breeder power plants would last as long a the Earth Sun relationship
Pu is used as a fuel, but Pu is also used in nuclear weapons
The radioactive fuel needs to be reprocessed, to extract the bred materials
  Safety issues during transportation and handling (environment, health, nuclear weapons)
There have also been practical problems
Notes: <number>

## Slide 53: Next Time
<number>
The Uranium Cycle
Safety
Accidents
Radiation and health
Fusion
Notes: <number>