## Slide 1: Last time: Digital devices
Introduction
Gate characteristics
Logic families
TTL
CMOS
Interfacing
Noise and EMC in digital systems
Chapter 26

## Slide 2
A graphical representation of noise immunity
Gate 1
output

## Slide 3
Timing considerations
  all gates have a certain propagation delay time, tPD
  this is the average of the two switching times

## Slide 4: A comparison of logic families Transistor-Transistor (TTL) Logic (bipolar) Metal oxide semiconductor (MOS) logic (FET)
TTL
1.5 – 33
Very good
122
10
NAND
1.5 – 200
TPD (ns)
Excellent
Noise immunity
1@1 MHz
>50
Fan-out
NAND-NOR
Basic gate
CMOS
Parameter
Power per gate (mW)
Notes: Power increases with speed in CMOS because more current needed to discharge capacitor
CMOS pPropagation delay times longer due to high output impedence = large RC. Lower the higher the voltage

## Slide 5
TTL inputs
  unused inputs, if left unconnected, will float to logical 1
  it is not advisable to allow them to float since they are then very susceptible to noise
  unused inputs should be tied directly to ground (logic 0) or through a resistor to the positive supply rail (logic 1)
    unused inputs to an AND or NAND gate should be tied high
    unused inputs to an OR or NOR gate should be tied low
  Can function as tri-state device (on, off, or not there!)
  Several variants of TTL available (e.g. Low-powered Schottky-TTL) that have many enhanced features.

## Slide 6
CMOS inputs
  CMOS gate protection circuitry
  CMOS inputs must not be left unconnected
  unused inputs should be tied directly to ground (logic 0) or to the positive supply rail (logic 1)
    unused inputs to an AND or NAND gate should be tied high
    unused inputs to an OR or NOR gate should be tied low
Can be easily “blown” with too high a voltage
Sensitive to static

## Slide 7: Noise and EMC in digital circuits
Designing digital systems for EMC
  backplane arrangements

## Slide 8: De-Coupling capacitors (between +Vcc and earth)
without
with

## Slide 9: Key points from digital devices ( = important)
Physical gates are not ideal components
Logic gates are manufactured in a range of logic families
The ability of a gate to ignore noise is its ‘noise immunity’
Both MOSFETs (FET) and bipolar junction transistors (BJT) are used in gates
MOS devices are voltage controlled, BJT current controlled
All logic gates exhibit a propagation delay
The most widely used logic families are TTL and CMOS.
Both TTL (BJT) and CMOS (FET) gates are produced in a range of versions, each optimised for a particular characteristic
Interface circuitry may be needed to link devices of different families
Noise and EMC issues must be considered during design

## Slide 10
Questions?

## Slide 11: Implementing digital systems
Introduction
Array logic
Microprocessors
System-on-a-chip devices
Selecting an implementation method
Chapter 27

## Slide 12: Introduction
In this lecture we will look at the techniques used to implement complex digital systems
We will begin by looking at the nature of various complex integrated circuits
The complexity of the integrated circuits used within electronic circuits is increasing rapidly
Available integration level increases exponentially with time (Moore’s Law)
27.1
Video 27A

## Slide 13: Moore’s Law
Integration densities of Intel microprocessors

## Slide 14: Names of Different Types of Array Logic (Names for information only, not tested)
Programmable logic devices (PLDs)
  these are examples of uncommitted logic
  forms include:
    programmable logic array (PLA)
    programmable array logic (PAL) 3,
    programmable read only memory (PROM)
    generic array logic (GAL)
    erasable programmable logic device (EPLD)
    programmable electrically erasable logic (PEEL)
    complex programmable logic device (CPLD)
    field programmable gate array (FPGA)
27.2
Re-programmable
Arrays of arrays

## Slide 15
Programmable logic array (PLA)
  has an array of inverters, AND gates and OR gates
  can implement any logic function (given limits on numbers of inputs and outputs)
  Example: consider a system with four inputs A, B, C and D and three output X, Y and Z, where
Video 27B

## Slide 16
  the structure of a simple PLA

## Slide 17
  the PLA programmed to give the required output functions
  the device is programmed by blowing fusible links at the various interconnection points

## Slide 18
  logic array shorthand symbolic notation

## Slide 19
  a PLA with 6 inputs, 4 outputs and 16 product terms

## Slide 20: Vocabulary
PLD Programmable logic device—types:
  PLA Programmable Logic Array
    Programmable array of AND and OR gates.
  PAL Programmable Array Logic
    Programmable array of AND gates and fixed array of OR gates.
  ROM Read Only Memory
    Fixed array of AND gates and programmable array of OR gates. (note PLA and PAL can be used as ROM)
Notes: Note, can make a ROM out of PLA and PAL

## Slide 21
Programming tools for array logic
  automated tools are used in almost all cases
  often make use of hardware description languages
  fuse maps are passed to a programmer to configure the device

## Slide 22
Custom and semi-custom ICs
  Some equipment may contain a custom IC designed by the manufacturer
  Others may have semi-custom or application specific integrated circuits (ASIC)
    produced by combining a number of standard cells (such as registers, counters, input/output circuitry and memory)
    much less costly than a complete design from scratch
As with PLD’s: Very difficult to find out what they do if you haven’t done the programming!

## Slide 23: Microprocessors (Top Level)
A microcomputer system
  the CPU takes the form of a microprocessor
27.3
Video 27E
Notes: Will be done in more detail in next lecture

## Slide 24
Communication within the microcomputer
Bus controller
Notes: Request access to bus from Bus controller

## Slide 25
Types of memory

## Slide 26
Random access memory (RAM)
  this is read-write memory
  write describes the process of storing information
  read describes the process of retrieval
  RAM is volatile in nature
  several forms:
    static RAM – uses circuitry similar to a bistable
    dynamic RAM – uses charge on capacitors, needs refreshing
  battery backup can be used to provide non-volatility

## Slide 27: What does the memory access look like?
Parallel
    Early memory chips contained one bit of many words
    Address one row and get one bit from each chip
1
1
0
1
1
0
1
1
Word at address 1
1
0
0
1
1
0
1
0
Word at address 2

## Slide 28
Dynamic random-access memory (DRAM)
More modern memory chips contained several bits (column) of many words (rows)
Address one row and get n bits of word from each chip

## Slide 29
Read-only memory (ROM)
  this can be read from, but not written to
  is inherently non-volatile (useful for programs, etc)
  many forms available
    some are programmed by the manufacturer (such as masked programmed devices)
    others are user programmable (such as EPROM, and EEPROM)
  memory such as EEPROM can be written to (programmed) as well as read, but it is not RAM
    it can only be programmed relatively slowly

## Slide 30
Example of addressing, reading, writing

## Slide 31
Example of addressing, reading, writing

## Slide 32
A 256x8 ram card is in the slop

## Slide 33
CPU has a list of addresses

## Slide 34
Each address in the RAM has information

## Slide 35
CPU puts the first address on the address bus

## Slide 36
Bus controller (not shown) gives access to CPU

## Slide 37
CPU enables ram to go to address

## Slide 38
Memory puts contents of address on bus for CPU to read

## Slide 39
CPU has the information

## Slide 40
Repeat the cycle to get next information

## Slide 44
Get next information

## Slide 48
CPU has received instruction to write information to memory address 01100100

## Slide 49
CPU puts address on address bus and information for that address on data bus

## Slide 50
CPU enables write

## Slide 51
Repeat as needed!

## Slide 61
Registers
  fundamental building blocks within computers
  can be constructed using D flip-flops
  some are used for storage, others for input/output

## Slide 62
Communications between registers
  achieved by enabling the output of one register and the input of another
  as all the registers are connected by the same data bus, only one piece of information can be transmitted at any time

## Slide 63: Input/Output
Interface
  Make the signals produced by the sensor compatible with those of the computer system.
  Make signals produced at the computer output suitable to drive the actuators directly.
The operations performed by the interface referred to as signal conditioning.
Video 27F

## Slide 64: Signal conditioning
Signal conditioning includes:
  Amplification (Chapter 14)
  Filtering to remove noise (Chapter 8)
  Isolation (Optical isolator Chapter 26.8.3)
  Analogue-to-digital and/or digital-to-analogue conversion (Chapter 28)

## Slide 65
Input/output
  The nature of the input/output section varies tremendously with the application.
  Input/output may use parallel or serial techniques.
  Parallel I/O often uses input/output registers which appear as simple memory locations to the processor
  Serial I/O for communication over longer distances. Can use a range of techniques including both synchronous and asynchronous methods.

## Slide 66: Serial I/O-parallel to serial  serial to parallel
Asynchronous serial communications
  Sender and receiver have (accurate) independent clocks
  Clocks at the same frequency
  The structure of an asynchronous word
At transition receiver starts its clock
Samples at same bit-rate at sender
Stop bit monitored for polarity

## Slide 67: Serial I/O
Synchronous serial communications
  Used for continuous stream of data
  Synchronization field sent to receiver
    A bit pattern or specific synchronization word
  Receiver clock then derived from sync-word/words

## Slide 68
Serial communications standards
  One of the most important standards is the Universal Serial Bus or USB
USB data is sent in packets Least Significant Bit (LSB) first.
There are 4 main USB packet types :Token, Data, Handshake and Start of Frame.
Each packet is constructed from different field types, namely SYNC, PID, Address, Data, Endpoint, CRC and EOP.
The packets are then bundled into frames to create a USB message.
For complete definition of data structure, if you need it, see:
TN_116_USB Data Structure.pdf on Blackboard-supplementary material.

## Slide 69
Programmed controlled input/output
  At some point program requires data from input device
  Data might not be ready at that time
  So: polling of I/O devices

## Slide 70
Video 27G
Interrupts
  the interrupt mechanism

## Slide 71
  multiple interrupt handling with a stack

## Slide 72: I/O techniques
Program controlled
  Simplest to implement and test
Interrupt-driven
  Fast response and less processor time than polling
  Hard to test as it is asynchronous
Direct memory access.
  Device accesses memory directly
  Little impact on processor time, but
  Extra interface hardware and expensive
  used for large transfers (disk drives etc.)

## Slide 73: Selecting an implementation method
The implementation method will depend on the complexity of the required functionality
  applications requiring just a handful of gates might use CMOS or TTL devices
  slightly more complex applications will often make use of array logic
  complex digital applications will probably use either complex programmable devices (such as CPLDs or FPGAs) or a microprocessor (or PLC).

## Slide 74: Next Lecture: Something to consider for simple dedicated machines
Raspberry Pi or Arduino
Credit card computer with video/TV, keyboard, USB and ethernet interface.
Developed for education/hobby (cheap)
Many plug-in resources available for interface
While developed for fun and learning, they are surprisingly sophisticated computers with a suite of interfaces available for control and sampling.
http://www.raspberrypi.org/
https://www.arduino.cc/

## Slide 75: Further Study
The Further Study section at the end of Chapter 27 considers the operation of a microcomputer-based controller in an automatic washing machine.
Your task is to decide how the device should control the speed of the motor.
Further Study
Video 27H
Decide which of the input/output techniques discussed earlier is most appropriate for this task and watch the video to assess your ideas.

## Slide 76: Key points
Available complexity doubles every couple of years.
Array logic integrates large numbers of gates within a single package that is then configured for a particular application.
Complex digital systems can also be implemented using a microcomputer.
A programmable logic controller is a self-contained microcomputer that is optimised for industrial control.
The implementation method used will depend on the complexity of the required system.

## Slide 77: Next week: Data acquisition and conversion
Introduction
Sampling
Signal reconstruction
Data converters
Sample and hold gates
Multiplexing
Chapter 28

## Slide 78: Introduction
Digital techniques have several advantages over analogue methods:
  They are less affected by noise
  Processing, transmission and storage is often easier
However, we often produce or use analogue signals
Therefore, we often have the need to translate between analogue and digital representations
28.1

## Slide 79: The sampling system
Abbreviations:
LPF = low pass filter
BPF = band pass filter
ADC = analogue to digital converter
DSP = digital signal processor
DAC = digital to analogue converter
Signal with maximum frequency F is filtered, sampled at frequency fs, digitized, stored and then output as an analogue signal that is filtered.
F
F
Notes: Think of a CD player

## Slide 80: The sampling system
Abbreviations:
LPF = low pass filter
BPF = band pass filter
ADC = analogue to digital converter
DSP = digital signal processor
DAC = digital to analogue converter
Signal with maximum frequency F is filtered, sampled at frequency fs, digitized, stored and then output as an analogue signal that is filtered.
F
F
Will talk about the DSP next lecture
Now we will first talk about the sampling and the filters
Then the ADC/DAC

## Slide 81: The sampling system
Abbreviations:
LPF = low pass filter
BPF = band pass filter
ADC = analogue to digital converter
DSP = digital signal processor
DAC = digital to analogue converter
Signal with maximum frequency F is filtered, sampled at frequency fs, digitized, stored and then output as an analogue signal that is filtered.
F
F
Why?
Notes: Think of a CD player

## Slide 82: Why the filters: Sampling
In order to obtain a picture of a varying quantity we need to take regular measurements
  this process is called sampling
  but how often do we need to sample?
The answer is given by the Nyquist sampling theorem which says that:
  the sampling rate must be greater than twice the highest frequency present in the signal being sampled.
  this minimum sampling rate is the Nyquist rate
28.2
Video 28A
Notes: Sample wave at period T
With sample time T

## Slide 83: Sampling
Sampling at frequency fs generates a
  A first harmonic extending to the Nyquist fny=fs/2
  A second harmonic (starting at fs)
But frequencies are both positive and negative
  The cos(2(-f)) = cos(2f); sin(2(-f)) = -sin(2f);
  Just a phase shift
So a signal at frequency f will appear at f in both the first and second harmonics

## Slide 84: Sampling at Ts gives a Nyquist at fny=1/(2Ts)
0
Ts
fny=1/(2Ts)
First harmonic
Sampling every Ts is a sampling frequency fs = 1/Ts

## Slide 85: Sampling at Ts also gives second harmonic fs=1/Ts
0
Ts
fny=1/(2Ts)
First harmonic
Second harmonic
fs=1/(Ts)
As long as highest frequency being sampled is at a frequency fo<fny, these harmonics do not overlap
Sampling every Ts is a sampling frequency fs = 1/Ts

## Slide 86: Have a signal of sine wave of period T=1/F
0
F
0
F
fS
2
fS
TS=1/fS
0
F
fS
fS
2
f
-FH
-FH
TS=1/fS
Now the 1st harmonic (at –FH) appears at fa = fS – F
It is “aliased” about the Nyquist frequency = fS/2

## Slide 87: First sample fast (Ts<T/2). How does this look in frequency?
0
F
0
F
fS
2
fS
TS=1/fS
0
F
fS
fS
2
f
-FH
-FH
TS=1/fS
Now the 1st harmonic (at –FH) appears at fa = fS – F
It is “aliased” about the Nyquist frequency = fS/2
0
Where |F| = |FH|
Still see it as a sine wave as long as I see peaks and valleys
Reach a limit when Ts = T/2just sample peak and valley each cycle
Then Tny = T (or fny = F ). Decreasing fs and moving it towards zero
Notes: At T, fs and moves closer to 0 ( Right axis moves  towards 0)
Note when Ts = T/2Tny = T
4 second sine wave sampled every 2 seconds

## Slide 88: Now sample at (Ts=T/2). How does this look in frequency?
0
F
0
F
fS
2
fS
f
-FH
TS=1/fS
Now the 1st harmonic (at –FH) appears at fa = fS – F
It is “aliased” about the Nyquist frequency = fS/2
0
Where |F| = |FH|
F =
fS
2
0
fS
-FH
0
TS=1/fS = T/2
TS=1/fS
Notes: At T, fs and moves closer to 0 ( Right axis moves  towards 0)
Note when Ts = T/2Tny = T
4 second sine wave sampled every 2 seconds

## Slide 89: Now sample slowly (Ts>T/2). How does this look in frequency?
0
F
0
F
fS
2
fS
TS=1/fS
0
F
fS
fS
2
f
-FH
-FH
TS=1/fS > T/2
Now the 1st harmonic (at –FH) appears at fa = fS – F
It is “aliased” about the Nyquist frequency = fS/2
We only really see 0-fNy
0
0

## Slide 90: If I sample slower than the Nyquist frequency
F
So a high-frequency signal at F Is read as a low frequency signal at fs-F
F

## Slide 91: “Negative” frequencies from harmonics
fs/2
fs
0
Power
-fs/2
-fs
-F
0
F
Fourier Transform
Shows power vs. frequency of sine wave at frequency F
Add a reverse scale of negative (1st harmonic) frequencies at -F
Notes: 0 Hz to 44100 Hz with a sample at 44100 Hz, Nyquist 20050 Hz

## Slide 92: “Negative” frequencies from harmonics
fs/2
fs
0
Power
-fs/2
-fs
0
Sine sweep 0-44kHz sampled at 44kHz
F
-F
Fourier Transform
Shows power vs. frequency of sine wave at frequency F
Add a reverse scale of negative (1st harmonic) frequencies at -F
Sweep a sine wave from 0-44 kHz, but sampled at 44 kHz
22 kHz
44 kHz
0 kHz
-22 kHz
0 kHz
-44 kHz
Notes: 0 Hz to 44100 Hz with a sample at 44100 Hz, Nyquist 20050 Hz
Anything above 20050 Hz will have red on left!

## Slide 93: “Negative” frequencies from harmonics
fs/2
fs
0
Power
-fs/2
-fs
0
Sine sweep 0-44kHz sampled at 22kHz
Fourier Transform
Shows power vs. frequency of sine wave at frequency F
Add a reverse scale of negative (1st harmonic) frequencies at -F
Sweep a sine wave from 0-44 kHz, but sampled at 44 kHz
Can hear the starred frequencies in the blue frequency range
22 kHz
44 kHz
0 kHz
F
*
-F
*
-22 kHz
0 kHz
-44 kHz
Notes: 0 Hz to 44100 Hz with a sample at 44100 Hz, Nyquist 20050 Hz

## Slide 94: “Negative” frequencies from harmonics
fs/2
fs
0
Power
-fs/2
-fs
0
Fourier Transform
Shows power vs. frequency of sine wave at frequency F
Add a reverse scale of negative (1st harmonic) frequencies at -F
Sweep a sine wave from 0-44 kHz, but sampled at 44 kHz
Can hear the starred frequencies in the blue frequency range
When harmonic frequency is at –F, it is heard at fs–F
22 kHz
44 kHz
0 kHz
-22 kHz
0 kHz
-44 kHz
-F
fs-F
F
F
F
F = 31 kHz, -F = -31 kHz, fs = 44 kHz Frequency heard = 44–31 = 13 kHz
Notes: 0 Hz to 44100 Hz with a sample at 44100 Hz, Nyquist 20050 Hz
Draw bottom sine and erase curve, keeping only the points

## Slide 95: Other examples of aliasing due to video sampling

## Slide 96
Note: the sampling rate is determined by the highest frequency present in the signal, Not the highest frequency of interest
If a signal contains unwanted high frequency components, we will see these as aliased frequencies. So they should be removed before sampling
  this is done using a low-pass filter
  such a filter is called an anti-aliasing filter
It is common to sample at about 20% or more above the Nyquist rate to allow for imperfect filtering

## Slide 97: Example of filtering
F
F
F
F
F
F
F
F
F
F
Specify the attenuation of the first harmonic in our “signal” band, 0F. (F  0.8fs/2 = 0.8fny)
Will still have those frequencies, but at an attenuation of DR.
Usually want as many frequencies as possible (Ffs/2), but that would require a sharp filter (“brick wall”),
Relax to ~80% of fny

## Slide 98: Example of filtering and “oversampling”
F
F
F
F
F
F
F
F
F
F
-3 dB
Remember, a LPF will have a -45 phase shift at the -3 dB point
If you want the violin at the same time as the bass, move this as far out as possible
A more gentle filter with same attenuation

## Slide 99: Next time: Data acquisition and conversion
Introduction
Sampling
Signal reconstruction
Data converters
Sample and hold gates
Multiplexing
Chapter 28