## Slide 1: Data acquisition and conversion
Introduction
Sampling
Signal reconstruction
Data converters
Sample and hold gates
Multiplexing
Chapter 28

## Slide 2: Introduction
Digital techniques have several advantages over analogue methods:
  They are less affected by noise
  Processing, transmission and storage is often easier
However, we often produce or use analogue signals
Therefore, we often have the need to translate between analogue and digital representations
28.1

## Slide 3: The sampling and conversion system
Abbreviations:
LPF = low pass filter
BPF = band pass filter
ADC = analogue to digital converter
DSP = digital signal processor
DAC = digital to analogue converter
Signal with maximum frequency F is filtered, sampled at frequency fs, digitized, stored and then output as an analogue signal that is filtered.
F
F

## Slide 4: Sampling
Sampling at frequency fs generates a
  A first harmonic extending to the Nyquist fny=fs/2
  A second harmonic (starting at fs)
Frequencies are both positive and negative
  The cos(2(-f)) = cos(2f); the sin(2(-f)) = -sin(2f)
  Just a phase shift
So a signal at frequency f will appear at f in both the first and second harmonics

## Slide 5: Sampling at Ts gives a Nyquist at fny=1/(2Ts)
0
Ts
fny=1/(2Ts)
First harmonic
Sampling every Ts is a sampling frequency fs = 1/Ts

## Slide 6: Sampling at Ts gives second harmonic fs=1/Ts
0
Ts
fny=1/(2Ts)
First harmonic
Second harmonic
fs=1/(Ts)
As long as highest frequency being sampled is at a frequency fo<fny, these harmonics do not overlap
Sampling every Ts is a sampling frequency fs = 1/Ts
(f-(fs-fo))
(f-(fs+fo))

## Slide 7: How does this look in frequency?
0
F
0
F
fS
2
fS
TS=1/fS
0
F
fS
fS
2
f
-FH
-FH
TS=1/fS
Now the 1st harmonic (at –FH) appears at fa = fS – F
It is “aliased” about the Nyquist frequency = fS/2
We only really see 0-fNy
0
0
Notes: See a film of a rotating spoked wheel

## Slide 8: Aliasing

## Slide 9: Input filtering of analogue to digital converter
Used to eliminate frequencies in the signal that are greater than the Nyquist frequency
Eliminates aliasing and is therefore called an anti-aliasing filter
“cleans up” the signal band and eliminates stray “noise” or aliased frequencies

## Slide 10: Example of filtering when sampling 20% above Nyquist limit (oversampling)
F
F
F
F
F
F
F
F
F
F
Specify the attenuation of the second harmonic in our “signal” band, 0F. (F  0.8fs/2 = 0.8fny)
Will still have those 2nd harmonic frequencies, but attenuated by DR.
Usually want as many frequencies as possible (Ffs/2), but that would require a sharp filter (“brick wall”),
Relax to F up to ~80% of fny
Notes: Filter must be sharp->phase distortion of the signal
Oversample a factor of 2 or 4 and
one can get the same DR with more gentle filter

## Slide 11: Output filtering
Converted analogue signal to digital numbers
Sampling “quantizes” the analogue signal into discrete steps
These “quanta” appear at the output of DAC giving us jumps
Low-pass filter to “smooth out” these stepsreconstruction filter
time

## Slide 12: Reconstruction filter

## Slide 13
Resolution of data converters
  a range of converters is available, each providing conversion to a particular resolution
  this determines the number of quantization levels used
  an n-bit converter uses 2n discrete steps
    e.g. an 8-bit converter uses 28 or 256 levels
    a 10-bit converter uses 210 or 1024 levels
  an 8-bit converter gives a resolution of about 0.4%
    volts/step = FullScaleVolts/(28 quantization levels)
    Resolution = volts/step/FSV *100 = 1/(28 quantization levels)

## Slide 14: Resolution vs. accuracy
The Resolution represents a “quantization” noise
Frequently quoted as ½ LSB
Accuracy will depend upon the total noise of the process, which depends on the entire chain (typically 1.5 LSB)
Reverse the chain through DAC for output

## Slide 15: How fast can we digitize or reconstruct a signal?
Determines what frequencies we can sample
Speed of conversion
  conversions of ADC’s or DAC’s take a finite time
  this is referred to as the conversion time or settling time of the converter
  the time taken depends on the converter
  DACs are usually faster than ADCs

## Slide 16
Digital-to-analogue converters (DACs)
  wide range of resolutions, but in general, conversion time increases with resolution
  a typical general-purpose 8-bit DAC would have a settling time of between 100 ns and 1 s
  a typical 16-bit converter would have a settling time of a few milliseconds
  for specialist applications high-speed converters have settling times of a few nanoseconds
  a video DAC might have a resolution of 8 bits and a maximum sampling rate of 100 MHz
Video 28B

## Slide 17
  a binary-weighted resistor DAC
If MSB = 1, all others 0, current to the op amp is I = –Vref/R
If next most MSB = 1 (others 0) , current is I = –Vref/(2R)
inverting amplifier changes Vo to null the current at the input  Vo = –I*RF
Op-Amp gain depends on which bits are = 1.
If just the LSB=1 gives I = –Vref/(2n-1R)
So for a binary input number m:

## Slide 18: Same idea, but same resistors for better thermal control
  an R-2R resistor chain DAC
A 1 on an input will cause a current to flow through the 2R resistor attached to the switch.
At the junction, this current sees an equivalent resistance 2R in each direction and is split equally
As it travels up the chain, it is split again at each junction
Coming from LSB it sees the most splitsthis gives the least current at op-amp
Op amp changes Vo to offset (null) the current at the input
Get a current proportional to the binary number

## Slide 19
Analogue-to-digital converters (ADCs)
  again available in a range of resolutions and speeds
  a typical 8-bit converter might have a settling time of between 1 and 10 s (~10x longer than a DAC)
  a typical 12-bit converter might have a settling time of 10 to 100 s
  But, high speed converters can exceed 150 million samples per second

## Slide 20
  a counter or servo ADC
Slow but cheap-few ms
Read counter
Note, the ADC contains a DAC, so it must be slower!

## Slide 21
  a successive approximation ADC (bisection)
  MSB=1, DAC = ½ scale, if less than input, keep MSB=1 & turn on next bit
  If more than input, reset bit to 0 and turn next bit on, keep going
Fast and still cheap
1-100 s for 8-12 bits
Most common type

## Slide 22
  a dual-slope ADC
Vi charges capacitor
Discharge at constant rate
Counter starts at start of discharge and stops at full discharge
Time = count = Vi
Slow (10-100 Hz) but very accurate

## Slide 23
  a parallel or flash ADC
Comparators connected to voltages with V>Vi produce one polarity,
All connected to V<Vi produce the opposite polarity.
Combinational logic is then used to determine the value of the input voltage from this pattern.
Go fast converter (ns)
Accurate and expensive

## Slide 24: Sample and hold gates
It is often useful to be able to sample a signal and then hold its value constant
  this is useful when performing analogue-to-digital conversion so that the signal does not change during conversion
  it is also useful when doing digital-to-analogue conversion to maintain the output voltage constant between conversions
This task is performed by a sample and hold gate
  we have looked at such circuits in earlier lectures
28.5

## Slide 25
A FET sample and hold gate
Hold time depends on:
  Conversion rate of ADC
  Signal frequency
Limiting conversion rate should be due to S/H jitter, bandwidth, distortion etc,
Not the encoder

## Slide 26
Most sample and hold gates are constructed using integrated circuits
Typical devices require a few microseconds to sample the incoming waveform, which then decays (or droops) at a rate of a few millivolts per millisecond
High speed devices, such as those used for video applications, can sample an input in a few nanoseconds, so droop must be limited to a few millivolts per microsecond

## Slide 27: Advantage of S/H
If signal is changing during conversion, increases bit errors, missing codes, and accentuates timing mismatches in comparators of flash ADC.
Encoder output
Output vs. input.

## Slide 28: Multiplexing
While some systems have a single input and a single output, often there are multiple inputs and outputs
Rather than have separate converters for each input and output, we often use multiplexing
  multiplexers make use of electrically operated switches to control the routing of signals
  these can be used at the input or output of a system
  normally separate anti-aliasing and/or reconstruction filters would be used with each input
28.6
Video 28C

## Slide 29
Input multiplexing
Time delay between sampled inputs

## Slide 30
Input multiplexing with sample and hold gates
All inputs sampled simultaneously—only droop to worry about (last one read has largest droop)

## Slide 31
Output multiplexing
Convert input 1-hold output 1
Get new input, convert new input, hold output on ch 2 …

## Slide 32
Single-chip data acquisition systems
  these are a combination of an ADC and a multiplexer within a single integrated circuit
  usually designed for use with microprocessor-based systems, and provide all the control lines necessary for simple interfacing
More info in the analogue devices analogue to digital conversion handbook on Blackboard analog_digital_conversion.zip

## Slide 33: Further Study
The Further Study section at the end of Chapter 28 looks at the use of analogue sensors within smartphones.
Consider what novel sensors could be added to a smartphone and suggest some applications that might make use of them.
Further Study
Video 28D
When you have given this some thought, take a look at the video.

## Slide 34: Key points
Converting an analogue signal to a digital form
  sampling the waveform and then performing
  Analogue to digital conversion
If sampling rate is above the Nyquist rate (> twice the highest frequency present), no information is lost as a result of sampling
When sampling broad spectrum signals we make use of anti-aliasing filters to remove unwanted components
When reconstructing signals, filters are used to remove the effects of the sampling
A wide range of ADCs and DACs is available
Sample and hold gates may be useful at the input or output
Multiplexers can reduce the number of converters required