## Slide 1: Last time: Data acquisition and conversion
Introduction
Sampling
Signal reconstruction
Data converters
Sample and hold gates
Multiplexing
Chapter 28

## Slide 2: Introduction
Analogue to Digital conversion (ADC) and Digital to Analogue Conversion (DAC)
Translate between analogue (voltage levels) and digital (binary number) representations
Allows us to store analogue information in computers
    Manipulate, display on screen, store digitally for future access
And allows us to recover digital information for play-back on analogue devices (stereo, video, meters, etc.)
28.1

## Slide 3: The sampling system
Abbreviations:
LPF = low pass filter
BPF = band pass filter
ADC = analogue to digital converter
DSP = digital signal processor
DAC = digital to analogue converter
Signal with maximum frequency F is filtered, sampled at frequency fs, digitized, stored and then output as an analogue signal that is filtered.
F
F
Notes: Think of a CD player

## Slide 4: Sampling
Sampling at frequency fs generates a
  A first harmonic extending to the Nyquist fny=fs/2
  A second harmonic (starting at fs)
But frequencies are both positive and negative
  The cos(2(-f)) = cos(2f); sin(2(-f)) = -sin(2f);
  Just a phase shift
So a signal at frequency f will appear at f in both the first and second harmonics

## Slide 5: Sampling at Ts also gives second harmonic fs=1/Ts
0
Ts
fny=1/(2Ts)
First harmonic
Second harmonic
fs=1/(Ts)
As long as highest frequency being sampled is at a frequency fo<fny, these harmonics do not overlap
Sampling every Ts is a sampling frequency fs = 1/Ts

## Slide 6: Now sample slowly (Ts>T). How does this look in frequency?
0
F
0
F
fS
2
fS
TS=1/fS
0
F
fS
fS
2
f
-FH
-FH
TS=1/fS
Now the 1st harmonic (at –FH) appears at fa = fS – F
It is “aliased” about the Nyquist frequency = fS/2
We only really see 0-fNy
0
0
No sampling
Proper Sampling
Under Sampling

## Slide 7: If I sample slower than the Nyquist frequency
F
So a high-frequency signal at F Is read as a low frequency signal at fs-F
F

## Slide 8: “Negative” frequencies from harmonics
fs/2
fs
0
Power
-fs/2
-fs
0
Sine sweep 0-44kHz sampled at 22kHz
Fourier Transform
Shows power vs. frequency of sine wave at frequency F
Add a reverse scale of negative (1st harmonic) frequencies at -F
Sweep a sine wave from 0-44 kHz, but sampled at 44 kHz
Can hear the starred frequencies in the blue frequency range
22 kHz
44 kHz
0 kHz
F
*
-F
*
-22 kHz
0 kHz
-44 kHz
Notes: 0 Hz to 44100 Hz with a sample at 44100 Hz, Nyquist 20050 Hz

## Slide 9: “Negative” frequencies from harmonics
fs/2
fs
0
Power
-fs/2
-fs
0
Fourier Transform
Shows power vs. frequency of sine wave at frequency F
Add a reverse scale of negative (1st harmonic) frequencies at -F
Sweep a sine wave from 0-44 kHz, but sampled at 44 kHz
Can hear the starred frequencies in the blue frequency range
When harmonic frequency is at –F, it is heard at fs–F
22 kHz
44 kHz
0 kHz
-22 kHz
0 kHz
-44 kHz
-F
fs-F
F
F
F
F = 31 kHz, -F = -31 kHz, fs = 44 kHz Frequency heard = 44–31 = 13 kHz
Notes: 0 Hz to 44100 Hz with a sample at 44100 Hz, Nyquist 20050 Hz
Draw bottom sine and erase curve, keeping only the points

## Slide 10: Other examples of aliasing due to video sampling

## Slide 11
Note: the sampling rate is determined by the highest frequency present in the signal, Not the highest frequency of interest
If a signal contains unwanted high frequency components, we will see these as aliased frequencies. So they should be removed before sampling
  this is done using a low-pass filter
  such a filter is called an anti-aliasing filter
It is common to sample at about 20% or more above the Nyquist rate to allow for imperfect filtering

## Slide 12: Noise considerations
Remember, much of our noise extends to high frequencies (white/red)
Has an amplitude at all frequencies, including above the Nyquist
Sample it, and we alias 2nd harmonic noise into the 1st harmonic
Even if we have all signal frequencies below the Nyquist, we will want to low-pass filter to remove the noise alias.
Amplitude mVolts
Amplitude Spectrum
Frequency (Hz)
0.5
1.0
fNy

## Slide 13: Example of filtering
F
F
F
F
F
F
F
F
F
F
Specify the attenuation of the first harmonic in our “signal” band, 0F. (F  0.8fs/2 = 0.8fny)
Will still have those frequencies, but at an attenuation of DR.
Usually want as many frequencies as possible (Ffs/2), but that would require a sharp filter (“brick wall”),
Relax to ~80% of fny

## Slide 14: Signal reconstruction
In many cases it is necessary to reconstruct an analogue signal from a series of sample
  typically after they have been processed, transmitted or stored
This requires the removal of the step transitions in the sampled waveform (step  high frequencies)
Reconstruction is achieved using a low-pass filter to remove these unwanted frequencies
  this filter is called a reconstruction filter
28.3

## Slide 15: Reconstruction filter

## Slide 16: Today: Data acquisition and conversion
Introduction
Sampling
Signal reconstruction
Data converters
Sample and hold gates
Multiplexing
Chapter 28

## Slide 17: What about the data converters!
Sampling involves taking a series of instantaneous measurements of a signal and converting these into a digital form
Reconstruction involves taking a series of digital readings and converting these back into their analogue equivalents
These two operations are performed by data converters which can be of two basic types:
  Analogue-to-digital converters (ADC’S)
  Digital-to-analogue converters (DAC’S)
28.4

## Slide 18: Resolution vs. accuracy
The Resolution represents a “quantization” noise
Frequently quoted as ½ LSB but need additional info: N-bits
Accuracy will depend upon the total noise of the process, which depends on the entire chain (typically 1.5 LSB)
Reverse the chain through DAC for output

## Slide 19
Resolution of data converters
  a range of converters is available, each providing conversion to a particular resolution
  this determines the number of quantization levels used
  an n-bit converter uses 2n discrete steps
    e.g. an 8-bit converter uses 28 or 256 levels
    a 10-bit converter uses 210 or 1024 levels
  an 8-bit converter gives a resolution of about 0.4%
    volts/step = FullScaleVolts / (28 quantization levels)
    Resolution = volts/step / FullScaleVolts *100 = 100/(28 quantization levels)
  Short cut: Resolution in % = 100 / 2n
Notes: Counts from 0 to 255, but that gives 256 steps

## Slide 20: How fast can we digitize or reconstruct a signal?
Determines what frequencies we can sample
Speed of conversion
  conversions of ADC’s or DAC’s take a finite time
  this is referred to as the conversion time or settling time of the converter
  the time taken depends on the converter
  DACs are usually faster than ADCs

## Slide 21
Digital-to-analogue converters (DACs)
  wide range of resolutions, but in general, conversion time increases with resolution
  a typical general-purpose 8-bit DAC would have a settling time of between 100 ns and 1 s
  a typical 16-bit converter would have a settling time of a few milliseconds
  for specialist applications high-speed converters have settling times of a few nanoseconds
  a video DAC might have a resolution of 8 bits and a maximum sampling rate of 100 MHz
Video 28B

## Slide 22
  a binary-weighted resistor DAC
A “1” on an input tries to draw current from the op amp junction (must come from Vo since input of op amp does not draw or source current)
Op amp changes Vo to null-out the current at the input
Just an inverting amplifier whose gain depends on which bits are 1.
Gain decreases from MSB to LSB
So for a binary input number m:
3 bit DAC

## Slide 23: Same idea, but use same resistor values for better thermal control
  an R-2R resistor chain DAC
A 1 on an input will cause a current to flow through the 2R resistor attached to the switch.
At the junction, this current sees an equivalent resistance 2R in each direction and is split equally
As it travels up the chain, it is split again at each junction
Coming from LSB it sees the most splitsthis gives the least current at op-amp (divided by 2n)
One split at the MSB, current divided by 2
Op amp changes Vo to offset (null) the current at the input
Digital word determines voltage here, VA
F

## Slide 24
Analogue-to-digital converters (ADCs)
  again available in a range of resolutions and speeds
  a typical 8-bit converter might have a settling time of between 1 and 10 s (~10x longer than a DAC)
  a typical 12-bit converter might have a settling time of 10 to 100 s
  But, high speed converters can exceed 150 million samples per second

## Slide 25
  a counter or servo ADC
Slow but cheap-few ms
Voltage here proportional to number of clock steps counted
When the 2 voltages equal
Stop the count

## Slide 26
  a successive approximation ADC (bisection)
  MSB=1, DAC = ½ scale, if less than input, keep MSB=1 & turn on next bit
  If more than input, reset bit to 0 and turn next bit on, keep going
Fast and still cheap
1-100 s for 8-12 bits
Most common type
Notes: Instead of always starting at 0
Go to ½ scale and work your way from there

## Slide 27
  a dual-slope ADC
Vi charges capacitor
Discharge at constant rate
Counter starts at start of discharge and stops at full discharge
Time = count = Vi
Slow (10-100 ms) but very accurate

## Slide 28
  a parallel or flash ADC
Comparators connected to voltages with V>Vi produce one polarity,
All connected to V<Vi produce the opposite polarity.
Combinational logic is then used to determine the value of the input voltage from this pattern.
Go fast converter (ns)
Accurate and expensive

## Slide 29: Sample and hold gates
It is often useful to be able to sample a signal and then hold its value constant
  this is useful when performing analogue-to-digital (ADC) conversion so that the signal does not change during conversion
  it is also useful when doing digital-to-analogue (DAC) conversion to maintain the output voltage constant between conversions
This task is performed by a sample and hold gate
  we have looked at such circuits in earlier lectures
28.5

## Slide 30
A FET sample and hold gate
Hold time depends on:
  Conversion rate of ADC
  Signal frequency
Limiting conversion rate should be due to S/H jitter, bandwidth, distortion etc,
Not the encoder

## Slide 31
Most sample and hold gates are constructed using integrated circuits
Typical devices require a few microseconds to sample the incoming waveform, which then decays (or droops) at a rate of a few millivolts per millisecond
High speed devices, such as those used for video applications, can sample an input in a few nanoseconds, so droop must be limited to a few millivolts per microsecond

## Slide 32: Advantage of S/H
If signal is changing during conversion, increases bit errors, missing codes, and accentuates timing mismatches in comparators of flash ADC.
Encoder output
Output vs. input.

## Slide 33: Multiplexing
While some systems have a single input and a single output, often there are multiple inputs and outputs
Rather than have separate converters for each input and output, we often use multiplexing
  multiplexers make use of electrically operated switches to control the routing of signals
  these can be used at the input or output of a system
  normally separate anti-aliasing and/or reconstruction filters would be used with each input
28.6
Video 28C

## Slide 34
Input multiplexing
Time delay between sampled inputs

## Slide 35
Input multiplexing with sample and hold gates
All inputs sampled simultaneously—only droop to worry about (last one read has largest droop)

## Slide 36
Output multiplexing
Convert input 1-hold output 1
Get new input, convert new input, hold output on ch 2 …

## Slide 37
Single-chip data acquisition systems
  these are a combination of an ADC and a multiplexer within a single integrated circuit
  usually designed for use with microprocessor-based systems, and provide all the control lines necessary for simple interfacing
More info in the analogue devices analogue to digital conversion handbook on It’s Learning analog_digital_conversion.zip

## Slide 38: Further Study
The Further Study section at the end of Chapter 28 looks at the use of analogue sensors within smartphones.
Consider what novel sensors could be added to a smartphone and suggest some applications that might make use of them.
Further Study
Video 28D
When you have given this some thought, take a look at the video.

## Slide 39: Key points
Converting an analogue signal to a digital form is achieved by sampling the waveform and then performing analogue to digital conversion
As long as the sampling rate is above the Nyquist rate (> twice the highest frequency present), no information is lost as a result of sampling
When sampling broad spectrum signals we make use of anti-aliasing filters to remove unwanted components
When reconstructing signals, filters are used to remove the effects of the sampling
A wide range of ADCs and DACs is available
Sample and hold gates may be useful at the input or output
Multiplexers can reduce the number of converters required

## Slide 41
The effects of sampling rate are illustrated here:
  (a) shows the original signal
  (b) shows the effects of sampling at a rate above the Nyquist rate
  (c) shows the effects of sampling at a rate below the Nyquist rate (fny=F/2)
  (d) Sample at the frequency of the sine wave, F, interpret as f=0 again! Second harmonic
F
F
TS=1/fS
TS=1/fS
So a high-frequency signal at F Is read as a low frequency signal at fs-F
Tny=1/(2F)

## Slide 42: “Negative” frequencies or harmonics
Fourier Transform
Shows power vs. frequency of sine wave at frequency F
Add a reverse scale of negative frequencies
A sine wave with high, negative frequency –F
Is heard as a low frequency sine wave at fs-F
fs/2
fs
0
Power
-fs/2
-fs
-F
fs-F
0
F
F
F
Sine sweep 0-44kHz sampled at 44 kHz
Notes: 0 Hz to 44100 Hz with a sample at 44100 Hz, Nyquist 20050 Hz