## Slide 1: Last Time: A/D converter design
Design considerations:
    When a voltage goes above certain levels, change a “bit”
    Have the bits change in a binary fashion
      Possibly some logic circuitry
    Precision voltage reference
    Sample (and therefore filter) and readout

## Slide 2: Key points
Converting an analogue signal to a digital form is achieved by sampling the waveform and then performing analogue to digital conversion
As long as the sampling rate is above the Nyquist rate (> twice the highest frequency present), no information is lost as a result of sampling
When sampling broad spectrum signals we make use of anti-aliasing filters to remove unwanted components
When reconstructing signals, filters are used to remove the effects of the sampling
A wide range of ADCs and DACs is available
Sample and hold gates may be useful at the input or output
Multiplexers can reduce the number of converters required

## Slide 3: Questions?
review

## Slide 4: Exam on 17 December 09:00-13:00
Digital home exam (see: https://innsida.ntnu.no/wiki/-/wiki/English/Digital+exam)
Format:
  25 multiple-choice homework style questions (4 pts each)
    No penalties  correct answer = 4, incorrect or blank answer = 0
You can have with you:
  Open book, open notes, anything you like!
Need 41% or better for pass (NTNU regulations)

## Slide 5: Key Points Chapter 3: Resistance & DC Circuits Be able to explain and do examples
An electric current is a flow of charge
A voltage source produces an e.m.f. which can cause a current to flow
Current in a conductor is directly proportional to voltage
Kirchoff’s laws
  At any instant the sum of the currents into a node is zero
  At any instant the sum of the voltages around a loop is zero
Any two terminal network of resistors and energy sources can be replaced by a Thévenin or Norton equivalent circuit
Nodal analysis and mesh analysis provide systematic methods of applying Kirchhoff’s laws

## Slide 6: Chapter 3
Solve simple circuits using either:
  Equivalent resistance
  Nodal analysis
  Mesh analysis
  Superposition
  Brute force of Ohm’s law
Use these techniques to get Thévenin or Norton equivalent circuit-Voc, Isc, Rth

## Slide 7: Key Points chapter 6- Alternating Voltages and Currents
A sinusoidal voltage waveform can be described by the equation
The voltage across a resistor is in phase with the current, the voltage across an inductor leads the current by 90, and the voltage across a capacitor lags the current by 90
The reactance of an inductor XL = L
The reactance of a capacitor XC = 1/C
The relationship between current and voltage in circuits containing reactance can be described by its impedance
The use of impedance is simplified by the use of complex notation or phase arithmetic

## Slide 8: AC Circuit Notation
v = v(t) Is the time dependent signal
Vp Is the peak signal
Vav Is the average over ½ cycle, where
V Is the Root Mean Square signal, where
The same relations apply to current: i(t), Ip, Iav and I
Frequently Vp and V are used interchangeably

## Slide 9
R
VR = IR
VR = IR
VC = -IXC
In parallel circuits, V is the same across all elements  I=V/R so V leading I in L  I lags V in L  IL = -V/XL
Sign of the phase is relative to the common element (V in parallel circuits, I in serial)
Consider these series circuits and phasor diagrams E leads I in L, I leads E in C

## Slide 10: Complex Notation
We can represent impedance using complex notation where
Resistors: ZR = R
Inductors: ZL = jXL = jL
Capacitors: ZC = -jXC =
6.6

## Slide 11
Series and parallel combinations of impedances
  impedances combine in the same way as resistors

## Slide 12: Key Points Chapter 7- Power in AC Circuits
In resistive circuits the average power is equal to VI, where V and I are r.m.s. values
In a capacitor the current leads the voltage by 90 and the average power is zero
In an inductor the current lags the voltage by 90 and the average power is zero
In circuits with both resistive and reactive elements, the instantaneous power is: and the average power or active power is VI cos 
The term cos  is called the power factor
Have the Active, Reactive and Apparent Power
Power factor correction is important in high-power systems
High-power systems often use three-phase arrangements

## Slide 13
Therefore
Active Power P = VI cos  watts
Reactive Power Q = VI sin  var
Apparent Power S = VI VA
S2 = P2 + Q2



## Slide 14: Or
You pay for the whole glass of beer in VA, but can only drink the W
Power factor = Amount of beer/Glass-size
var
(
(
(
(
Active Power (W)
(var)

## Slide 15: What lags and what leads?
Basis for Comparison | Leading Power Factor | Lagging Power Factor
Basic | The load current leads the supply voltage by certain phase angle. | There is a phase difference between voltage and current where load current lags the supply voltage.
Nature of load in electrical circuit | Capacitive | Inductive
Correction of low power factor | By the addition of inductive load. | By adding capacitive load.
Value of power factor | Exists between -1 to 0. | Exists between 0 and 1.
Reactive component | Negative | Positive
Examples of respective loads | Capacitive load: Electrical motors, capacitor, radio circuits, etc. | Inductive load: Power generator, inductor, relays, etc.
Taken as the current relative to voltage

## Slide 16: Key Points Chapter 8- Frequency Characteristics of AC Circuits
The reactance of capacitors and inductors is dependent on frequency
Single RC or RL networks can produce an arrangement with a single upper or lower cut-off frequency
In each case the angular cut-off frequency o is given by the reciprocal of the time constant 
For an RC circuit  = CR, for an RL circuit  = L/R
Resonance occurs when the reactance of the capacitive element cancels that of the inductive element
Simple RC or RL networks represent single-pole filters
Stray capacitance and inductance are found in all circuits

## Slide 17: AC circuits—should be able to:
Calculate transfer functions for complex impedances
Know cutoff and resonance frequencies, resonance conditions, bandwidth.
Draw Bode plots of the transfer function
Remember: High FrequenciesXL, XC0
Low Frequencies XC, XL0

## Slide 18: Gain—should be able to define (as a ratio or in dB):
We then define voltages and currents at the input and output
Then
Unknown
System

## Slide 19
Know the resonant frequencies of series and parallel RLC circuits
Know whether the resonant condition is a maximum (parallel) or minimum (series) impedance
Know the quality factor, Q for each circuit and how it relates to bandwidth.
    this is the ratio of the power stored (in L or C) to the power dissipated (in R) in each cycle

## Slide 20: Key Points Chapter 9-Transient Behaviour
The charging or discharging of a capacitor, and the energising and de-energising of an inductor, are each associated with exponential voltage and current waveforms
Circuits that contain resistance, and either capacitance or inductance, are termed first-order systems
The increasing or decreasing exponential waveforms of first-order systems can be described by the initial and final value formulae
Circuits that contain both capacitance and inductance are usually second-order systems. These are characterised by their undamped natural frequency and their damping factor

## Slide 21
A comparison of the four circuits

## Slide 22: Be able to describe the response of First-Order Systems
Know Initial and final value formulae (& how to use)
  increasing or decreasing exponential waveforms (for either voltage or current) are given by:
  where Vi and Ii are the initial values of the voltage and current
  where Vf and If are the final values of the voltage and current
  the first term in each case is the steady-state response
  the second term represents the transient response
  the combination gives the total response of the arrangement

## Slide 23: Second-Order Systems—define
Circuits containing both capacitance and inductance are normally described by second-order differential equations. These are termed second-order systems
  for example, this circuit is described by the equation
  Or general form:
   = damping factor
9.5
vR+vL+vC = V and vL=L(di/dt), and vR=iR but i = C(dvC/dt). So
   =1 critically damped

## Slide 24: Key points Chapter 14- Amplification
Amplification forms part of most electronic systems
Amplifiers may be active or passive
Equivalent circuits are useful when investigating the interaction between circuits
The gain of all amplifiers falls at high frequencies
The gain of some amplifiers falls at low frequencies
Differential amplifiers take as their input the difference between two input signals
Some amplifiers are very simple in construction

## Slide 25
Construct an equivalent circuit of the amplifier, the source and the load to calculate loading effects
  Vi divided between Ri and Rs, Vo between Ro and RL
  Amplifier gain is Av, but Actual gain of circuit is Vo / Vi
An ideal voltage amplifier and would have: Av = , Ri =  and Ro = 0, But real ones have realistic values

## Slide 26: Key points Chapter 15- Control and feedback
Feedback is used in almost all automatic control systems
Feedback can be either negative or positive
If the gain of the forward path is A, the gain of the feedback path is B and the feedback is subtracted from the input then
If AB is positive and much greater than 1, then G  1/B
Negative feedback can be used to overcome problems of variability within active amplifiers
Negative feedback can be used to increase bandwidth, and to improve other circuit characteristics

## Slide 27
  therefore the bandwidth increases as the gain is reduced with feedback
  in some cases the gain x bandwidth = constant
A
G

## Slide 28: Key points Chapter 16-Operational amplifiers
Operational amplifiers are among the most widely used building blocks in electronic circuits
An ideal operational amplifier would have infinite voltage gain, infinite input resistance and zero output resistance
Real op-amps have several non-ideal characteristics However, if we choose components appropriately this should not affect the operation of our circuits
Feedback allows us to increase bandwidth by trading gain against bandwidth (gain-bandwidth product & unity gain bandwidth)
Feedback also allows us to alter other circuit characteristics for the better
Analysis of op-amp circuits using ideal amplifiers

## Slide 29: Basic operational amplifier circuits
Two Basic Rules
  1)An Op-Amp will do whatever is necessary with its output to adjust the voltage at its inverting input so that it is equal to the voltage at its non-inverting input. I.e. make the voltage difference between its inputs equal to zero.
  2)Op-Amp inputs draw virtually no current (0.2nA to fA). (For an ideal op-amp Iin = 0)
Horowitz, Paul and Hill, Winfred,The Art of Electronics, Cambridge University Press, 1980

## Slide 30: Op-amp circuits
Be able to apply the aforementioned rules to calculate gain or other circuit properties of op-amp circuits with feedback applied.

## Slide 31: Key points Chapter 17: Semiconductors and diodes
Diodes allow current to flow in only one direction
Doping of semiconductors leads to the production of p-type and n-type materials
How a junction between p-type and n-type semiconductors creates the properties of a diode
Behaviour of silicon semiconductor diodes approximate the ideal diodes but have a conduction voltage of about 0.7 V
How diodes work under forward and reverse bias
Vocabulary, terms and operation of p-n junctions and diodes
I-V behaviour of diodes and equivalent circuits
Diode circuits

## Slide 32: Doping of semiconductors
Pure semiconductors
  Electrons freed by thermal motions are negative charge carriers
  Holes left behind that accept adjacent electrons are positive charge carriers
  Few charge carriers at room temperature  poor conductors under intrinsic conduction
Doping
  the addition of small amounts of impurities drastically affects its properties
  some materials form an excess of electrons and produce an n-type semiconductor and the electrons are the majority carrier
  some materials form an excess of holes and produce a p-type semiconductor and the holes are the majority carrier
  both n-type and p-type materials are neutral but have much greater conductivity than pure semiconductors
  this is extrinsic conduction

## Slide 33: p-type and n-type materials joined to form pn junction
  Majority charge carriers diffuse across (diffusion current) and recombine leaving the ionized dopants behind
  The dopants have opposite charge, resulting in an Electric Field or potential barrier across the junction.
  This impedes the diffusion of further charge carriers
  The result is a depletion or space charge layer with intrinsic conduction
  Thermally generated charge pairs swept by Ē producing drift current that is balanced by diffusion current so Inet=0
E

## Slide 34
Thus,
  at room temperature e/kT ~ 40 V−1
If V > + 0.1 V,
If V < – 0.1 V,
  IS is the reverse saturation current
That is, our drift or thermal current, Is
VON=0.7V

## Slide 35: Diodes—should be able to:
Effect on E-fields, internal potentials of forward and reverse bias
Explanation of current vs voltage curves including breakdown
Equivalent circuits of diodes
Zener diodes-what they are and how to calculate current, voltage and power requirements
Describe and Explain output of diode circuits

## Slide 36: Key points Chapter 18 Field-effect transistors
FETs are widely used in both analogue and digital circuits
They have high input resistance and small physical size
There are two basic forms of FET: MOSFETs and JFETs
MOSFETs may be divided into DE and Enhancement types
In each case the gate voltage controls the current from the drain to the source
The characteristics of the various forms of FET are similar except that they require different bias voltages
DC analysis of bias
AC analysis requires equivalent circuit
  VDS coupled to ground by capacitance

## Slide 37: FET
Basic operation, input and output characteristics
Identify types of FET (JFET, DE-Mosfet, E-Mosfet)
Areas of Id vs Vds where FET can be safely operated
DC and Small signal analysis

## Slide 38
FET output characteristics
Above here the channel thickness is  0 at drain
More VDS gives no more current
Here channel has resistance set by VGS
Here ID ~independent of the applied voltage & controlled by VGS
Small slope = Rout
Need to set a DC (quiescent) operating point
for the small signal (AC) variations of vgs
Know why this point should avoid the Ohmic, High ID and High VDS regions

## Slide 39: Key points Chapter 19- Bipolar junction transistors
Bipolar transistors are widely used in both analogue and digital circuits
How the p-n junctions work in a BJT
They can be considered as either voltage-controlled or current-controlled devices
Their characteristics may be described by their gain or by their transconductance
Feedback can be used to overcome problems of device variability
Again, must set DC (quiescent) bias, and use equivalent circuit to calculate small-signal (AC-signal) gain
Input and output characteristics, where on Ic vs Vce curve it can be safely operated

## Slide 40
Output characteristics
  region near to the origin is the saturation region
  this is normally avoided in linear circuits by selecting DC-operating point
  slope of lines represents the output resistance
magnified
IC  linear with IB
Typical operating point
Why in this region?

## Slide 41: Comparison of FET and Bipolar
 | Field Effect Transistor (FET) | Bipolar Junction Transistor (BJT)
1 | Low voltage gain | High voltage gain
2 | High current gain | Low current gain
3 | Very high input impedance | Low input impedance
4 | High output impedance | Low output impedance
5 | Low noise generation | Medium noise generation
6 | Fast switching time | Medium switching time
7 | Easily damaged by static | Robust
8 | Some require an input to turn it “OFF” | Requires zero input to turn it “OFF”
9 | Voltage controlled device | Current controlled device
10 | Exhibits the properties of a Resistor | 
11 | More expensive than bipolar | Cheap
12 | Difficult to bias | Easy to bias

## Slide 42: Key points Chapter 22-Noise
Noise in electronic circuits can be of various forms, including thermal noise, shot noise, 1/f noise and interference—know their properties
Both bipolar transistors and FETs suffer from noise
Noise can be picked from radiated noise (high frequency) or poor grounding schemes (loops or serial grounding)
Circuit layout plays a major role in determining EMC performance
Signal to noise, and noise figure

## Slide 43: Last time: Device noise
Thermal or Johnson noise
  Random thermal motion of charge carriers in resistive materials (both BJT and FET’s)
  Gaussian and white
Shot noise (current noise)
  Statistical fluctuations in the number of charge carriers flowing
  Most apparent at low current levels
  Source of noise in BJT transistors from low IB flow across p-n potential barriers.
  ~Gaussian and white
1/f noise
  Variety of sources.
  Most common is flicker noise, the variation of diffusion of charge carriers in devices
  Common source of noise in FET devices
  Power increases at low frequencies  “red” (6dB/octave) or “pink” (3dB/octave) noise

## Slide 44: Figures of merit
Signal quality: Signal to noise ratio
  Average voltage level divided by RMS noise:
  Expressed in dB as:
  Can get Vs by averaging input samples
Circuit quality: Noise figure
  Measured output RMS noise divided by Measured input RMS noise times the gain of the circuit:

## Slide 45: Key points Chapter 23- Positive feedback, oscillators and stability
Positive feedback is used in the production of oscillators
The requirement for oscillation is that the loop gain AB must have a magnitude of 1, and a phase shift of 180 (or 180 plus some integer multiple of 360)
This can be achieved using a circuit that produces a phase shift of 180 subtracted from a non-inverting amplifier’s feedback (or added to an inverting amplifier’s feedback)
Alternatively, it can be achieved using a circuit that produces a phase shift of 0 subtracted from an inverting amplifier’s feedback (or added to a non-inverting amplifier’s feedback)
For good frequency stability we often use crystals
Care must be taken to ensure the stability of all feedback systems. What are gain and phase margins
Types of oscillators and how they work

## Slide 46: Key points Chapter 24-Digital systems- combinational logic
Logic circuits are usually implemented using logic gates
Circuits in which the output is determined solely by the current inputs are termed combinational logic circuits
Logic functions can be described by truth tables or using Boolean algebraic notation to create logic circuits
Boolean expressions can often be simplified by algebraic manipulation, or using techniques such as Karnaugh maps
Binary digits may be combined to form digital words that can be processed using binary arithmetic
Know how to go between truth table, Boolean expression, Karnaugh map and logic circuit

## Slide 47: Combinational logic building blocks
Know the logic gates, their truth tables and their Boolean expressions
Construct a logical function from a truth table
Implement function with gates (e.g. gates that do: )
Reverse  translate a gate system to a logical function
Simplify expressions algebraically or using a Karnaugh map

## Slide 48: Key points Chapter 23-Sequential logic
Sequential logic circuits have the characteristic of memory
Among the most important groups of sequential components are the various forms of multivibrator
  Bistables-flip flops and latches
  Monostables-one shots
  Astables-digital oscillators and timers
Know what these are and how they work (input vs. output)
Recognize them in a circuit or logical diagram
Be able to draw output waveforms for a given input
Know what shift registers do and how to do serialparallel
Know what ripple and modulo counters do and how

## Slide 49
Example 2-The J-K flip-flop
  Similar to S-R flip-flop but toggles when J = K = 1

## Slide 50: Key points Chapter 24-Digital devices
Physical gates are not ideal components
The ability of a gate to ignore noise is its ‘noise immunity’ Know what that is and how to calculate
All logic gates exhibit a propagation delay
  Know what causes this
The most widely used logic families are TTL and CMOS.
  Know general properties of each
Interface circuitry may be needed to link devices of different families
Noise and EMC issues must be considered during design
  Know what to do with unused inputs

## Slide 51: A comparison of logic families Transistor-Transistor (TTL) Logic (bipolar) Metal oxide semiconductor (MOS) logic (FET)
1.5 – 200
1.5 – 33
TPD (ns)
Excellent
Very good
Noise immunity
1@1 MHz
1 – 22
Power per gate (mW)
>50
10
Fan-out
NAND-NOR
NAND
Basic gate
CMOS
TTL
Parameter
Know what these terms mean!

## Slide 52: Key points Chapter 25- Implementing digital systems
Array logic integrates large numbers of gates within a single package that is then configured for a particular application
Complex digital systems can also be implemented using a microcomputer
The implementation method used will depend on the complexity of the required system
General ideas and implementation: control & data bus, microprocessor, ram, synchronous and asynchronous I/O
Define synchronous ad –asynchronous serial communication and how they differ.

## Slide 53: Key points Chapter 28- Data acquisition and conversion
Converting an analogue signal to a digital form is achieved by sampling the waveform and then performing analogue to digital conversion
As long as the sampling rate is above the Nyquist rate (> twice the highest frequency present), no information is lost as a result of sampling
When sampling broad spectrum signals we make use of anti-aliasing filters to remove unwanted components
When reconstructing signals, reconstruction filters are used to remove the effects of the sampling
A wide range of ADCs and DACs is available
Sample and hold gates may be useful at the input or output
Multiplexers can reduce the number of converters required

## Slide 54: Should be able to describe:
Resolution of ADC
The sampling system
Nyquist sampling rate and aliasing
Anti aliasing and reconstruction filters
Sample and hold gates (good & bad features)
Typical speeds for ADC and DAC

## Slide 55: And Finally

## Slide 56
Best of Luck
And thanks for a great class!