## Slide 1: Last time
Circuit solving methods
AC circuits

## Slide 2: Circuit Solving Methods Choice of Techniques
How do we choose the right technique?
  nodal and mesh analysis will work in a wide range of situations but are not necessarily the simplest methods
  Sometimes superposition/brute force is easiest
  no simple rules
  often involves looking at the circuit and seeing which technique seems appropriate
3.13

## Slide 3: AC Circuit Notation
v = v(t) Is the time dependent signal
Vp Is the peak signal
Vav Is the average over ½ cycle, where
V Is the Root Mean Square signal, where
Frequently Vp and V are used interchangeably

## Slide 4: Key Points of AC circuits
A sinusoidal voltage waveform can be described by the equation
The voltage across a resistor is in phase with the current, the voltage across an inductor leads the current by 90, and the voltage across a capacitor lags the current by 90
The reactance of an inductor XL = L
The reactance of a capacitor XC = 1/C
The relationship between current and voltage in circuits containing reactance can be described by its impedance
The use of impedance is simplified by the use of complex notation

## Slide 5: CIVIL (CI leads V; L V lead I) or ELI the ICE man (E leads I in L, I leads E in C)
sin(t+90)
sin(t-90)
Relative to applied Current: VL leads I, VC lags I
Relative to applied Voltage: IL lags V, IC leads V
Notes: Relative to Current: VL leads I, VC lags I
Relative to Voltage: IL lags VL, IC leads VC

## Slide 6: This time
Examples of Reactance
Accounting for Phase
Examples of impedance (Chapter 6)
Power in AC circuits (Chapter 7)

## Slide 7: Ignoring the phase and looking at peak Vp and Ip
Since reactance represents the ratio of voltage to current it has units of ohms
The reactance of a component can be used in much the same way as resistance:
  for an inductor
  for a capacitor

## Slide 8
Example – see Example 6.3 from course text
A sinusoidal voltage of 5 V peak and 100 Hz is applied across an inductor of 25 mH. What will the peak current be?
At this frequency, the reactance of the inductor is given by
Therefore
Remember, here we are ignoring the phase angle and only looking at the peak!
But the peak voltage in a capacitor will occur at a different time than the peak voltage in the resistor or inductor

## Slide 9: Phasor Diagrams (account for )
Sinusoidal signals are characterized by their magnitude, their frequency and their phase
In many circuits the frequency is fixed (perhaps at the frequency of the AC supply) and we are interested in only magnitude and phase
In such cases we often use phasor diagrams which represent magnitude and phase within a single diagram
6.4

## Slide 10: Phasor Diagrams (account for )
Examples of phasor diagrams
(a) here L represents the magnitude and  the phase of a sinusoidal signal
Same current in R, L and C (i.e. they are in series)
Relative to applied Current: VL leads I, VC lags I

## Slide 11: Phasor Diagrams (account for )
Examples of phasor diagrams
(a) here L represents the magnitude and  the phase of a sinusoidal signal
(b) shows the voltages across a resistor, an inductor and a capacitor for the same sinusoidal current
sin(t+90)
sin(t-90)
Reactive axis
Resistive axis
No big deal, just vector addition
Instead of x & y components, have resistive and reactive components
Same current in R, L and C (i.e. they are in series)
Relative to applied Current: VL leads I, VC lags I

## Slide 12
Phasor diagrams can be used to represent the addition of signals. This gives both the magnitude and phase of the resultant signal

## Slide 13
Phasor diagrams can also be used to show the subtraction of signals

## Slide 14: Phasor analysis of RL and RC series circuits Current the same in both what is the voltage?
Phasor analysis of an RL circuit
See Example 6.5 in the text for a numerical example
(RMS but same relation for Vp or Vrms)
V
 = tan-1(+VL/VR) and V = (VR2 + VL2)½
Relative to applied Current: VL leads I, VC lags I

## Slide 15: Phasor analysis of RL and RC series circuits Current the same in both what is the voltage?
Phasor analysis of an RC circuit
See Example 6.6 in the text for a numerical example
 = tan-1(-VC/VR) and V = (VR2 + VC2)½
V
Relative to applied Current: VL leads I, VC lags I

## Slide 16: What’s happening?
V is the source voltage and it is out of phase with I in circuit?
Why? Because there are 2 voltage sources here driving current:
  AC power supply
  Charged capacitor
When power supply is at 0 V, the capacitor is charged and it drives its own current in the circuit.
  Even though vS=0, vC0 and drives a current
  Hence i0 in the circuit and vR0

## Slide 18: Phasor analysis of RLC series circuits Current the same in both what is the voltage?
Phasor analysis of an RLC circuit

## Slide 19: Phasor analysis of RL and RC series circuits Current the same in both what is the voltage?
Current R = Current L  E leads I in L  positive 
Current R = Current C  I leads E in C ( E lags I in C)  negative 

## Slide 20
Voltage and current are in phase across resistor
Current leads voltage across the capacitor
vR and i
vC
vR
vC

## Slide 21
Voltage and current are in phase across resistor
Current leads voltage across the capacitor
Across the pair
vR and i
vC
vseries
vR
vC
vseries
vseries

## Slide 22
Voltage and current are in phase across resistor
Current leads voltage across the capacitor
Across the pair
vR and i
vC
vseries
vseries
vseries
vR
vC
vseries
Remember

## Slide 23: Phasor analysis of RLC series circuits Current the same in both what is the voltage v?
Phasor analysis of an RLC circuit-total v =

## Slide 24: Simple RLC series circuit
vseries(t) = vR(t) + vL(t) + vC(t),
The current i(t) is sinusoidal, as before.
The voltage across the resistor, vR(t), is in phase with the current.
Voltage across the inductor, vL(t), is 90° ahead and
Voltage across the capacitor, vC(t), is 90° behind.
R
L
C
vseries(t)

## Slide 25: What’s happening in the RLC series circuit
Phasor shows the resultant rms voltage and phase
R
L
C
Amplitude of vector sum:
V2series = V2R + (VL - VC)2

## Slide 26: What happens when VL = VC in RLC series circuit
The voltages in the resistor and capacitor cancel out!
The series voltage only appears across the resistor
All power is dissipated by the resistor (I and V in phase)
R
L
C
Amplitude of vector sum:
V2series = V2R + (VL - VC)2 So: V2series = V2R IF VL = VC called resonance

## Slide 27
Phasor analysis of parallel circuits
in such circuits the voltage across each of the components is the same and it is the currents that are of interest
Phasor analysis of RL and RC parallel circuits
Voltage the same over both  what is the current?
Relative to applied Voltage: IL lags V, IC leads V
Relative to applied Voltage: IL lags V, IC leads V

## Slide 28: What happens when |VL| = |VC|
The voltages in the resistor and capacitor cancel out!
The series voltage only appears across the resistor
All power is dissipated by the resistor (I and V in phase)
R
L
C
Amplitude of vector sum:
V2series = V2R + (VL - VC)2 So: V2series = V2R IF VL = VC called resonance

## Slide 29: Simple RLC parallel circuit
Parallel RLC circuits, V is the same across all
  as before
Relative to applied Voltage: IL lags V, IC leads V
Notes: 1/(jL) + 1/(-j/(C)) = -j/(L) + 1/(1/(jC))
= -j/(L) + j(C)

## Slide 30: Simple RLC parallel circuit
Parallel RLC circuits, V is the same across all
  as before
Relative to applied Voltage: IL lags V, IC leads V
Notes: 1/(jL) + 1/(-j/(C)) = -j/(L) + 1/(1/(jC))
= -j/(L) + j(C)

## Slide 31: What happens when |IL|=|IC| in RLC parallel circuit
Parallel RLC circuits, V is the same across all
  The currents through L and C can cancel and the only current would flow through R
  Only R would dissipate the power since i and v in phase
iR=i
iL
iC
IL+IC=0
Notes: 1/(jL) + 1/(-j/(C)) = -j/(L) + 1/(1/(jC))
= -j/(L) + j(C)

## Slide 32: Impedance
In circuits containing only resistive elements the current is related to the applied voltage by the resistance of the arrangement
In circuits containing reactive, as well as resistive elements, the current is related to the applied voltage by the impedance, Z of the arrangement
  this reflects not only the magnitude of the current but also its phase
  impedance can be used in reactive circuits in a similar manner to the way resistance is used in resistive circuits
6.5

## Slide 33: Phasor analysis of RL series circuit Current the same in both what is the voltage?
Consider the following circuit and its phasor diagram
R
Relative to applied Current: VL leads I, VC lags I

## Slide 34: Phasor analysis of RL series circuit Current the same in both what is the voltage?
Consider the following circuit and its phasor diagram
R
Relative to applied Current: VL leads I, VC lags I

## Slide 35
From the phasor diagram it is clear that that the magnitude of the voltage across the arrangement V is
where
Z is the magnitude of the impedance, so Z =|Z|
A constant of proportionality between V and I. The Impedance

## Slide 36
From the phasor diagram the phase angle of the impedance is given by
This circuit contains an inductor but a similar analysis can be done for circuits containing capacitors
In general
and
Sign from diagram

## Slide 37
A graphical representation of impedance

## Slide 38: What if we have R, L and C in both series and parallel?
Phasors get messy
But, phasors (vectors) look like complex numbers
  Instead of adding x and y (or resistive and reactive) components separately , we add real and imaginary components
  Vertical axis (reactive) is imaginary with j = (-1)½
We will combine them using the Impedance, which we derive from the Reactance

## Slide 39: Complex Notation- Carries magnitude and phase information
Phasor diagrams are similar to Argand Diagrams used in complex mathematics
We can also represent impedance using complex notation where
Resistors: ZR = R
Inductors: ZL = jXL = jL
Capacitors: ZC = -jXC =
6.6
The j tells us it is reactive

## Slide 40
Graphical representation of complex impedance

## Slide 41: Before we took Vpconstant*Ip with the constant of proportionality either R XL or XC
Resistor Inductor Capacitor
But we needed to add phase information
Now contains that phase information where
or

## Slide 42
Series and parallel combinations of impedances
  impedances combine in the same way as resistors

## Slide 43: Series and Parallel Impedances
Zseries = Z1 + Z2 + Z3 + …Zn
    Doesn’t matter if Z is from a Resistor, Inductor or Capacitor
    The complex reactance corrects
1/Zparallel = 1/Z1 + 1/Z2 + 1/Z3 + …Zn
    Doesn’t matter if Z is from a Resistor, Inductor or Capacitor
    The complex reactance corrects

## Slide 44
Manipulating complex impedances
  complex impedances can be added, subtracted, multiplied and divided in the same way as other complex quantities
  they can also be expressed in a range of forms such as the rectangular, polar and exponential forms
  if you are unfamiliar with the manipulation of complex quantities (or would like a little revision on this topic) see Appendix D of the course text which gives a tutorial on this subject

## Slide 45
Example – see Example 6.7 in the course text
Determine the complex impedance of this circuit at a frequency of 50 Hz
At 50Hz, the angular frequency  = 2f = 2 50 = 314 rad/s
Therefore

## Slide 46
A further example
  A more complex task is to find the output voltage of this circuit
  The analysis of this circuit, and a numerical example based on it, are given in Section 6.6.4 and Example 6.8 of the course text

## Slide 47: Key Points of AC circuits
A sinusoidal voltage waveform can be described by the equation
The voltage across a resistor is in phase with the current, the voltage across an inductor leads the current by 90, and the voltage across a capacitor lags the current by 90
The reactance of an inductor XL = L
The reactance of a capacitor XC = 1/C
The relationship between current and voltage in circuits containing reactance can be described by its impedance
The use of impedance is simplified by the use of complex notation

## Slide 48: Further Study
The Further Study section at the end of Chapter 6 looks at the characteristics of a simple reactive circuit.
See if you can model the behaviour of the circuit at a single frequency and then watch the video to check your analysis.
Further Study
Video 6B

## Slide 49: Next time: Power in AC Circuits
    Introduction
    Power in Resistive Components
    Power in Capacitors
    Power in Inductors
    Circuits with Resistance and Reactance
    Active and Reactive Power
    Power Factor Correction
    Three-Phase Systems
    Power Measurement
Chapter 7

## Slide 50: Introduction
The instantaneous power dissipated in a component is a product of the instantaneous voltage and the instantaneous current
p = vi
In a resistive circuit the voltage and current are in phase – calculation of p is straightforward
In reactive circuits, there will normally be some phase shift between v and i, and calculating the power becomes more complicated
7.1

## Slide 51: Power in Resistive Components
Suppose a voltage v = Vp sin t is applied across a resistance R. The resultant current i will be
The resultant instantaneous power p will be
7.2
(that is, p(t) = i(t)v(t))

## Slide 52
Calculate the average power over a ½ cycle ( = t)
where V and I are the r.m.s. voltage and current
From Chapter 2
Vavg=(2/)Vp
Vrms=(1/2)Vp
Same for Current

## Slide 53
Relationship between v, i and p in a resistor

## Slide 54: Power in Capacitors
From our discussion of capacitors we know that the current leads the voltage by 90. Therefore, if a voltage v = Vp sin t is applied across a capacitance C, the current will be given by i = Ip cos t
Then
The average power over t = 0 is zero
7.3

## Slide 55
Relationship between v, i and p in a capacitor

## Slide 56: Power in Inductors
From our discussion of inductors we know that the current lags the voltage by 90. Therefore, if a voltage v = Vp sin t is applied across an inductance L, the current will be given by i = -Ip cos t
Therefore
Again the average power is zero
7.4

## Slide 57
Relationship between v, i and p in an inductor

## Slide 58: Circuit with Resistance and Reactance
When a sinusoidal voltage v = Vp sin t is applied across a circuit with resistance and reactance, the current will be of the general form i = Ip sin (t - )
Therefore, the instantaneous power, p is given by
7.5
Notes: X=phi, Y = 2wt-phi
(X+Y)/2= wt
(X-y)/2 = -(wt-phi)
Sin([-(wt-phi)] = -sin(wt-phi)
Therefore
cos(phi)-cos(2wt-phi) = -2sin(wt)sin(wt-phi)

## Slide 59
The expression for p has two components
The second part oscillates at 2 and has an average value of zero as t goes from 0 to 1 full cycle
  this is the power that is stored in the reactive elements and then returned to the circuit within each cycle
The first part represents the power dissipated in resistive components. Average power dissipation is

## Slide 60
The average power dissipation given by
is termed the active power in the circuit and is measured in watts (W)
The product of the r.m.s. voltage and current VI is termed the apparent power, S. To avoid confusion this is given the units of volt amperes (VA)

## Slide 61
From the above discussion it is clear that
In other words, the active power is the apparent power times the cosine of the phase angle.
This cosine is referred to as the power factor

## Slide 62: Active and Reactive Power
When a circuit has resistive and reactive parts, the resultant power has 2 parts:
  The first is dissipated in the resistive element. This is the active power, P
  The second is stored and returned by the reactive element. This is the reactive power, Q , which has units of volt amperes reactive or var
While reactive power is not dissipated it does have an effect on the system
  for example, it increases the current that must be supplied and increases losses with cables
7.6

## Slide 63
Consider an RL circuit
  the relationship between the various forms of power can be illustrated using a power triangle
Applied voltage V
If VR=Vcos() then
VL=Vsin() since there is a 90 phase shift between VR and VL

## Slide 64
Therefore
Active Power P = VI cos  watts
Reactive Power Q = VI sin  var
Apparent Power S = VI VA
S2 = P2 + Q2

## Slide 65: Power Factor Correction
Power factor (Active/Apparent power) is particularly important in high-power applications
Inductive loads have a lagging power factor
Capacitive loads have a leading power factor
Many high-power devices are inductive
  a typical AC motor has a power factor of 0.9 lagging
  the total load on the national grid is 0.8-0.9 lagging
  this leads to major inefficiencies
  power companies therefore penalize industrial users who introduce a poor power factor
7.7

## Slide 66
The problem of poor power factor is tackled by adding additional components to bring the power factor back closer to unity
  a capacitor of an appropriate size in parallel with a lagging load can ‘cancel out’ the inductive element
  this is power factor correction
  a capacitor can also be used in series but this is less common (since this alters the load voltage)
  for examples of power factor correction see Examples 7.2 and 7.3 in the course text

## Slide 67: Three-Phase Systems
So far, our discussion of AC systems has been restricted to single-phase arrangement
  as in conventional domestic supplies
In high-power industrial applications we often use three-phase arrangements
  these have three supplies, differing in phase by 120
  phases are labeled red, yellow and blue (R, Y & B)
7.8

## Slide 68
Relationship between the phases in a three-phase arrangement

## Slide 69
Three-phase arrangements may use either 3 or 4 conductors

## Slide 70: Power Measurement
When using AC, power is determined not only by the r.m.s. values of the voltage and current, but also by the phase angle (which determines the power factor)
  consequently, you cannot determine the power from independent measurements of current and voltage
In single-phase systems power is normally measured using an electrodynamic wattmeter
  measures power directly using a single meter which effectively multiplies instantaneous current and voltage
7.9

## Slide 71
In three-phase systems we need to sum the power taken from the various phases
  in three-wire arrangements we can deduce the total power from measurements using 2 wattmeters
  in a four-wire system it may be necessary to use 3 wattmeters
  in balanced systems (systems that take equal power from each phase) a single wattmeter can be used, its reading being multiplied by 3 to get the total power

## Slide 72: Who cares?
In Europe, the standard is TT or TN-C earthing
In Norway (and perhaps Albania) it is IT earthing
Buy equipment with TT or TN-C
You will need an additional transformer to run it in Norway

## Slide 73: Further Study
The Further Study section at the end of Chapter 7 is concerned with power factor correction for a high-power motor.
Your task is to calculate the size of capacitor needed to achieve a specific power factor.
Do the sums and then watch the video.
Further Study
Video 7B

## Slide 74: Key Points
In resistive circuits the average power is equal to VI, where V and I are r.m.s. values
In a capacitor the current leads the voltage by 90 and the average power is zero
In an inductor the current lags the voltage by 90 and the average power is zero
In circuits with both resistive and reactive elements, the average power is VI cos 
The term cos  is called the power factor
Power factor correction is important in high-power systems
High-power systems often use three-phase arrangements